| Heli-Inter Inc. 6500 Chemin de la Savane St-Hubert (Québec) J3Y 8Y9 GST / TPS: 133608992RT0002 QST / TVQ: 1013621574TQ0002 Ph. Office: 450-468-3431 Fax:450-468-5497 Comptabilite@heli-inter.com | C-FZXY Detailed View Registration C-FZXY Date Oct 6, 2017 Make EUROCOPTER TTAF 11207.7 Model AS350BA Serial No. 2082 | Actions 12M - 12M-Inspection 24M - 24M-Inspection Ann - Annual up-date Bi- - Bi-Annual Test Cap - Capacity test Che - Check Cle - Clean/inspect OR replace INF - INF Ins - Inspection O/C - O/C OC - OC OTL - OTL Ove - Overhaul Rep - Replacement Ret - Retirement Ser - Service SLL - SLL var - various |
| --- | --- | --- |

| Cycles values |
| --- |
| Cycle Name | Value | Cycle Name | Value | Cycle Name | Value | Cycle Name | Value |
| ENG. - (HOURS) | 6 564.7 | ENG_#1_NG | 15 278.1 | ENG_#1_NP | 19 172.7 | External loads | 26.0 |
| HOBBS | 0.0 | HOOK TIME - (hours) | 29.2 | Landings | 28 564.0 | TORQUE CYCLES | 28 590.0 |

| Components |
| --- |
| Component/Action | Make/Model | Part No. | Serial No. | Tracking No. | Limit | Perf. | Time at Inst. | Due | TTSC | TTSN | Rem. |
| A.A.I.R. / Ann | / |  |  |  | 12.0M | Mar 1, 17 |  | Mar 1, 18 | 7.2M |  | 4.8M |
| ANTI-VIBRATOR ASSY / Ins 6200 | / | 350A31-0033-06 | VIK36309 |  | 3000.0H 72.0M* | 9883.7H Sep 20, 11 * | 0.0H * | 12883.7H Feb 24, 18 * | 1324.0H 72.5M* | * | 1676.0H 4.6M* |
| BLADE M/R (#1) / Ret 6200 | / | 355A11-0020-00 |  |  | 20000.0H |  |  |  |  |  | 10000H |
| BLADE M/R (#2) / Ret 6200 | / | 355A11-0020-00 |  |  | 20000.0H |  |  |  |  |  | 10000H |
| BLADE M/R (#3) / Ret 6200 | / | 355A11-0020-00 |  |  | 20000.0H |  |  |  |  |  | 10000H |
| CARGO HOOK / Ove Cycle Name : HOOK TIME - (hours) | ONBOARD SYSTEMS/ | 528-023-01 | 384 | 27513 | 60.0M 1000.0C | 10908.4H May 13, 15 25.4C | 0.0H | May 13, 20 1025.4C | 299.3H 28.8M 3.8C |  | 31.2M 996.2C |
| -- ELT 406AF / 12M 2500 | / | S1840501-01 | 2620237-0293 | 24117 | 12.0M | Jun 21, 17 |  | Jun 21, 18 | 3.5M |  | 8.5M |
| COMPASS SWING / Ser 053000 | / |  |  |  | 12.0M | 11187.8H Jul 28, 17 |  | Jul 28, 18 | 19.9H 2.3M |  | 9.7M |
| Engine (ARRIEL 1B) / O/C 7100 **Linked AD: 2014-0036 | TURBOMECA/ ARRIEL 1B | 0292005060 | 4354 | 22536 |  | 11083.7H Feb 25, 16 | 7667.7H |  | 7791.7H 19.4M | 7791.7H |  |
| -- 100-HOUR inspection (ENGINE #1) / 0500 | / |  |  |  | 100.0H 12.0M | 11187.8H Jul 28, 17 |  | 11287.8H Jul 28, 18 | 19.9H 2.3M |  | 80.1H 9.7M |
| -- 3rd 100-HOUR inspection (ENGINE #1) / 0500 | / |  |  |  | 300.0H | 11083.7H Feb 25, 16 | 72.7H 5.6 | 11311.0H | 196.7H 25.0M |  | 103.3H |
| -- 600-HOUR inspection (ENGINE #1) / 0500 | / |  |  |  | 600.0H | 11083.7H Mar 8, 16 |  | 11683.7H | 124.0H 18.9M |  | 476.0H |
| -- ENG oil FILTER (ARRIEL 1B) / Cle 7900 | / | 9560158180 |  |  | 100.0H | 11176.6H Aug 9, 16 |  | 11276.6H | 31.1H 13.9M |  | 68.9H |
| -- ENGINE OIL (Mobil 254) (ARRIEL 1B) / Rep 7900 | / |  |  |  | 300.0H 24.0M | 11187.8H Jul 28, 17 |  | 11487.8H Jul 28, 19 | 19.9H 2.3M |  | 280.1H 21.7M |
| -- ENGINE VIBRATION (ARRIEL 1B) / Che 0500 | / |  |  |  | 750.0H | 11083.7H Feb 25, 16 |  | 11833.7H | 124.0H 19.4M |  | 626.0H |
| -- FCU CHARACTERISTICS (ARRIEL 1B) / Che 0500 | / | TASK 73-21-00-820-801 |  |  | 500.0H | 11084.5H Mar 8, 16 |  | 11584.5H | 123.2H 18.9M |  | 376.8H |
| -- FREEWHEEL SHAFT ASSY (3600H) (ARRIEL 1B) / Ove 7100 | / | 0292907550 | 898B |  | 3600.0H | 11083.7H Feb 25, 16 | 719.0H 0.3 | 13964.7H | 843.0H 19.6M |  | 2757.0H |
| -- FUEL CONTROL UNIT (3000H/120M) (ARRIEL 1B) / Ove 7300 | TURBOMECA/ ARIEL 1B | 0164850900 | C384B | 8011 | 3000.0H 120.0M | 11083.7H Feb 25, 16 | 201.5H 10.8 | 13882.2H Mar 30, 25 | 325.5H 30.2M |  | 2674.5H 89.8M |
| -- MO-1 ACCESSORY GEARBOX (ARRIEL 1B) / Ove 7200 | / | 70BM011080 | 4101 |  | 180.0M | 11083.7H Feb 25, 16 | 9900.1H 143.3 | Mar 16, 19 | 10024.1H 162.7M | 10024.1H | 17.3M |
| -- MO-2 AXIAL COMPRESSOR (ARRIEL 1B) / Ove 7200 | / | 70BM021060 | 4374 |  | 6000.0H 180.0M | 11083.7H Feb 25, 16 | 2208.2H 128.8 | 14875.5H May 30, 20 | 2332.2H 148.2M | 5519.6H | 3667.8H 31.8M |
| -- MO-3 GAS GENERATOR (ARRIEL 1B) / Ove 7200 | / | 70BM031090 | 4373 |  | 3000.0H 180.0M | 11083.7H Feb 25, 16 | 2208.2H 128.8 | 11875.5H May 30, 20 | 2332.2H 148.2M | 7012.7H | 667.8H 31.8M |
| -- MO-4 FREE TURBINE (ARRIEL 1B) / Ove 7200 | / | 70BM041030 | 1901 |  | 6000.0H 180.0M | 11083.7H Feb 25, 16 | 4486.8H 110.1 | 12596.9H Dec 21, 21 | 4610.8H 129.5M | 6320.5H | 1389.2H 50.5M |
| -- MO-5 REDUCTION GEARBOX (ARRIEL 1B) / Ove 7200 | / | 70BM055020 | 4562 |  | 3000.0H 180.0M | 11083.7H Feb 25, 16 | 1557.7H 110.1 | 12526.0H Dec 21, 21 | 1681.7H 129.5M | 7791.7H | 1318.3H 50.5M |
| -- OIL SCAVENGE TUBE CLEANING, task 72-43-00-610-801 (#1) / Ins | / | 72-43-00-610-801 |  |  | 1000.0H | 11083.7H Feb 25, 16 | 715.1H 0.3 | 11368.6H | 839.1H 19.6M |  | 160.9H |
| -- OVERSPEED DRAIN VALVE (ARRIEL 1B) / Ove 7600 | TURBOMECA/ | 0174126090 | M747910 | 8020 | 120.0M | 11187.8H Jul 28, 17 |  | Jul 28, 27 | 19.9H 2.3M |  | 117.7M |
| -- PERMEABILITY check of the injection manifold (ARRIEL 1B) / che 0500 | / |  |  |  | 750.0H | 11083.7H Feb 25, 16 |  | 11833.7H | 124.0H 19.4M |  | 626.0H |
| -- START DRAIN VALVE (ARRIEL 1B) / Ove 7300 | / | 0174078030 | C494B |  | 120.0M | Feb 25, 16 | 72.6 | Feb 7, 20 | 91.9M |  | 28.0M |
| ENGINE INLET AIR FILTER SYSTEM (STC SR00811SE) / OC 7200 | FDC/Aerofilter/ AS350/355 |  |  |  |  |  |  |  |  |  |  |
| -- AIR FILTER ELEMENT (STC SR00811SE) / OTL 7100 | FDC AIRFILTER/ AS350 | 1350A2-1 | 01234 | 29761 | 4500.0H | 11156.4H Jul 8, 16 | 1227.0H 0.0 | 14429.4H | 1278.3H 14.9M |  | 3221.7H |
| EPICYCLIC (3500-HR) / Ove 6300 | / | 350A32-0110-00 | M1501 |  | 3500.0H 288.0M | 9628.3H Mar 25, 10 | 0.0H | 13128.3H Mar 25, 34 | 1579.4H 90.4M |  | 1920.6H 197.6M |
| FIRE EXTINGUISHER (SLL=120M) / Ret 2600 | / | IEX253 | ZT-703910 | 33885 | 120.0M | Jul 27, 17 |  | Jul 27, 27 | 2.3M |  | 117.7M |
| FIRST AID KIT / Ins 2500 | / | PS-KIT | HI-PS-047 | 27820 | 12.0M* | 11187.8H Jun 22, 17 * | * | Jun 22, 18 * | 19.9H 3.5M* | * | 8.5M* |
| FUEL BOOST PUMP / Ins 2820 | / | P94B12-208 | 20587 |  | 2400.0H | 9883.7H | 0.0H | 12283.7H | 1324.0H |  | 1076.0H |
| FUEL FILTER ELEMENT,A/F / Ret 2820 | PUROLATOR/ | 1763440 | 7363780953 | 30713 | 1000.0H 48.0M | 11002.1H Aug 25, 15 |  | 12002.1H Aug 25, 19 | 205.6H 25.4M |  | 794.4H 22.6M |
| HOSES (RUBBER/POLYAMIDE, all) / Ret | / | RUBBER/POLYAMIDE |  |  | 144.0M | May 24, 08 |  | May 24, 20 | 112.4M |  | 31.6M |
| HYD. OIL FILTER (A) / Ret 2900 | / | 806966 |  |  | 600.0H 24.0M | 11045.8H Oct 30, 15 | 0.0H | 11645.8H Oct 30, 17 | 161.9H 23.2M |  | 438.1H 0.8M |
| HYDRAULIC BELT / OTL 2900 | / | POLYV597K4 |  |  | 1800.0H 72.0M | 9883.7H Apr 4, 12 | 0.0H | 11683.7H Apr 4, 18 | 1324.0H 66.1M |  | 476.0H 5.9M |
| HYDRAULIC HOSES (074239) / 2900 | PTFE/ |  |  |  |  |  |  |  |  |  |  |
| -- HYDRAULIC HOSE (D) / O/C 2900 | AIRBUS HELICOPTER TEXTRON/ | 704A34412256 | L201407465 | 20157 | * | 10605.2H Oct 3, 14 * | * | Oct 31, 23 * | 602.5H 36.1M* | * | 72.8M* |
| -- HYDRAULIC HOSE (E) / O/C 2900 | AIRBUS HELICOPTER TEXTRON/ | 704A34412252 | 01.04.2013 | 20440 | * | 10605.2H Oct 3, 14 * | * | Apr 30, 23 * | 602.5H 36.1M* | * | 66.8M* |
| -- HYDRAULIC HOSE (F) / O/C 2900 | AIRBUS HELICOPTER TEXTRON/ | 704A34412256 | L201407465 | 20157 | * | 10605.2H Oct 3, 14 * | * | Oct 31, 23 * | 602.5H 36.1M* | * | 72.8M* |
| -- HYDRAULIC HOSE (G) / O/C 2900 | AIRBUS HELICOPTERE/ | 704A34-412-256 | L201606650 | 41253 | * | 11187.8H Jul 27, 17 * | * | Jul 31, 25 * | 19.9H 2.3M* | * | 93.8M* |
| -- ALTIMETRE / 24M 3400 | UNITED INSTRUMENT/ | 5934P-3 | 445436 | 26175 | 24.0M | Jul 27, 17 |  | Jul 27, 19 | 2.3M |  | 21.7M |
| -- - 5400-HR (skids) / Ins 0500 | / |  |  |  | 5400.0H | 9883.7H Apr 4, 12 |  | 15283.7H | 1324.0H 66.1M |  | 4076.0H |
| -- - 5400HR (shock absorbers) / Ins 0500 | / |  |  |  | 5400.0H | 9883.7H Apr 4, 12 |  | 15283.7H | 1324.0H 66.1M |  | 4076.0H |
| -- BLADE HORN (#1) / Ret 622000 | / | 350A31-1877-02 | M7117 |  | 80000.0H | 0.0H | 0.0H | 80000.0H | 11207.7H |  | 68792.3H |
| -- BLADE HORN (#2) / Ret 622000 | / | 350A31-1877-02 | M7390 |  | 80000.0H | 0.0H | 0.0H | 80000.0H | 11207.7H |  | 68792.3H |
| -- BLADE HORN (#3) / Ret 622000 | / | 350A31-1877-02 | M7409 |  | 80000.0H | 0.0H | 0.0H | 80000.0H | 11207.7H |  | 68792.3H |
| -- SLEEVE LOWER FLANGE (straight) (#1) / Ret 622000 | / | 350A31-1850-02 | M9140 |  | 6600.0H | 6930.5H | 0.0H | 13530.5H | 4277.2H |  | 2322.8H |
| -- SLEEVE LOWER FLANGE (straight) (#2) / Ret 622000 | / | 350A31-1850-02 | M9884 |  | 6600.0H | 6930.5H | 0.0H | 13530.5H | 4277.2H |  | 2322.8H |
| -- SLEEVE LOWER FLANGE (straight) (#3) / Ret 622000 | / | 350A31-1850-02 | M10007 |  | 6600.0H | 6930.5H | 0.0H | 13530.5H | 4277.2H |  | 2322.8H |
| -- SLEEVE UPPER FLANGE (straight) (#1) / Ret 622000 | / | 350A31-1850-03 | M9844 |  | 6600.0H | 6930.5H | 0.0H | 13530.5H | 4277.2H |  | 2322.8H |
| -- SLEEVE UPPER FLANGE (straight) (#2) / Ret 622000 | / | 350A31-1850-03 | M9810 |  | 6600.0H | 6930.5H | 0.0H | 13530.5H | 4277.2H |  | 2322.8H |
| -- SLEEVE UPPER FLANGE (straight) (#3) / Ret 622000 | / | 350A31-1850-03 | M9575 |  | 6600.0H | 6930.5H | 0.0H | 13530.5H | 4277.2H |  | 2322.8H |
| -- Spherical Thrust Bearing (#1) / Ret 622000 | / | 704A33-633-21151 | 11083 |  | 6400.0H | 9319.5H | 0.0H | 15719.5H | 1888.2H |  | 4511.8H |
| -- Spherical Thrust Bearing (#2) / Ret 622000 | / | 704A33-633-21151 | 10231 |  | 6400.0H | 9319.5H | 0.0H | 15719.5H | 1888.2H |  | 4511.8H |
| -- Spherical Thrust Bearing (#3) / Ret 622000 | / | 704A33-633-21151 | 11272 |  | 6400.0H | 9319.5H | 0.0H | 15719.5H | 1888.2H |  | 4511.8H |
| -- Spherical Thrust Bearing Bolt (#1) / Ret 622000 | / | 350A31-1854-21 | 50386 |  | 3000.0H | 9883.7H | 0.0H | 12883.7H | 1324.0H |  | 1676.0H |
| -- Spherical Thrust Bearing Bolt (#2) / Ret 622000 | / | 350A31-1854-21 | 45682 |  | 3000.0H | 9883.7H | 0.0H | 12883.7H | 1324.0H |  | 1676.0H |
| -- Spherical Thrust Bearing Bolt (#3) / Ret 622000 | / | 350A31-1854-21 | 45717 |  | 3000.0H | 9883.7H | 0.0H | 12883.7H | 1324.0H |  | 1676.0H |
| -- Spherical Thrust Bearing Bolt (#4) / Ret 622000 | / | 350A31-1854-21 | 42313 |  | 3000.0H | 9883.7H | 0.0H | 12883.7H | 1324.0H |  | 1676.0H |
| -- Spherical Thrust Bearing Bolt (#5) / Ret 622000 | / | 350A31-1854-21 | 50436 |  | 3000.0H | 9883.7H | 0.0H | 12883.7H | 1324.0H |  | 1676.0H |
| -- Spherical Thrust Bearing Bolt (#6) / Ret 622000 | / | 350A31-1854-21 | 45739 |  | 3000.0H | 9883.7H | 0.0H | 12883.7H | 1324.0H |  | 1676.0H |
| -- STARFLEX (2400H) / Ret 622000 | / | 350A31-1918-00 | M75 |  | 2400.0H | 10389.2H | 0.0H | 12789.2H | 818.5H |  | 1581.5H |
| MAIN ROTOR MAST ASSY / OC 623000 **Linked AD: 2014-0132R1 | / | 350A37-0004-02 | M205 |  |  | 0.0H |  |  | 11207.7H |  |  |
| -- - SB05.00.32, shaft corrosion insp. / Ins 0500 | / |  |  |  | 72.0M | 11187.8H Jul 28, 17 |  | Jul 28, 23 | 19.9H 2.3M |  | 69.7M |
| -- MAIN ROTOR SHAFT (B) / SLL 623000 Cycle Name : TORQUE CYCLES | / | 350A37-1290-02 | M2873 |  | 160000.0C | 12598.0C | 0.0C | 172598.0C | 15992.0C |  | 144008.0C |
| -- SWASHPLATE BEARING (6300H) / OTL 623000 | / | Y51BB10843S2M74 | NR8868 |  | 6300.0H | 9628.3H | 0.0H | 15928.3H | 1579.4H |  | 4720.6H |
| MGB BEVEL REDUCTION GEAR (post MOD 07 7175) / Ove 6300 | / | 350A32-0300-04 | M2282 |  | 3500.0H 288.0M | 9628.3H Apr 16, 10 | 0.0H | 13128.3H Apr 16, 34 | 1579.4H 89.7M | 5077.2H | 1920.6H 198.3M |
| -- MRH attachment bolt (#1) / Ret 623000 | / | 350A37-1244-20 | 75066 |  | 3000.0H | 8582.3H | 0.0H | 11582.3H | 2625.4H |  | 374.6H |
| -- MRH attachment bolt (#2) / Ret 623000 | / | 350A37-1244-20 | 67137 |  | 3000.0H | 8582.3H | 0.0H | 11582.3H | 2625.4H |  | 374.6H |
| -- MRH attachment bolt (#3) / Ret 623000 | / | 350A37-1244-20 | 75231 |  | 3000.0H | 8582.3H | 0.0H | 11582.3H | 2625.4H |  | 374.6H |
| -- MRH attachment bolt (#4) / Ret 623000 | / | 350A37-1244-20 | 75277 |  | 3000.0H | 8582.3H | 0.0H | 11582.3H | 2625.4H |  | 374.6H |
| -- MRH attachment bolt (#5) / Ret 623000 | / | 350A37-1244-20 | 67154 |  | 3000.0H | 8582.3H | 0.0H | 11582.3H | 2625.4H |  | 374.6H |
| -- MRH attachment bolt (#6) / Ret 623000 | / | 350A37-1244-20 | 67159 |  | 3000.0H | 8582.3H | 0.0H | 11582.3H | 2625.4H |  | 374.6H |
| -- MRH attachment bolt (#A) / Ret 623000 | / | 350A37-1245-20 | 58012 |  | 3000.0H | 8582.3H | 0.0H | 11582.3H | 2625.4H |  | 374.6H |
| -- MRH attachment bolt (#B) / Ret 623000 | / | 350A37-1245-20 | 69139 |  | 3000.0H | 8582.3H | 0.0H | 11582.3H | 2625.4H |  | 374.6H |
| -- MRH attachment bolt (#C) / Ret 623000 | / | 350A37-1245-20 | 58007 |  | 3000.0H | 8582.3H | 0.0H | 11582.3H | 2625.4H |  | 374.6H |
| -- MRH attachment bolt (#D) / Ret 623000 | / | 350A37-1245-20 | 69035 |  | 3000.0H | 8582.3H | 0.0H | 11582.3H | 2625.4H |  | 374.6H |
| -- MRH attachment bolt (#E) / Ret 623000 | / | 350A37-1245-20 | 69040 |  | 3000.0H | 8582.3H | 0.0H | 11582.3H | 2625.4H |  | 374.6H |
| -- MRH attachment bolt (#F) / Ret 623000 | / | 350A37-1245-20 | 60648 |  | 3000.0H | 8582.3H | 0.0H | 11582.3H | 2625.4H |  | 374.6H |
| OIL PUMP, MGB / Ove 6300 | / | 350A32-0400-00 | M2393 |  | 3500.0H 288.0M* | 9628.3H Apr 16, 10 * | 0.0H * | 13128.3H Apr 16, 34 * | 1579.4H 89.7M* | * | 1920.6H 198.3M* |
| SERVO M/R (AC) (#1) / Ove 6700 | DUNLOP/ MAIN ROTOR | AC67246 | PR007 | 24670 | 1800.0H 240.0M | 11187.8H Jul 28, 17 | 1038.2H 55.1 | 11949.6H Dec 26, 32 | 1058.1H 57.3M |  | 741.9H 182.7M |
| SERVO M/R (AC) (#2) / Ove 6700 | / | AC67244 | RE160 | 34657 | 1800.0H 240.0M | 11083.7H Feb 25, 16 | 474.0H 36.8 | 12409.7H Jan 29, 33 | 598.0H 56.2M | 5511.0H | 1202.0H 183.8M |
| SERVO M/R (AC) (#3) / Ove 6700 | DUNLOP/ | AC67244 | AN202 |  | 1800.0H 240.0M | 10187.5H Aug 2, 12 |  | 11987.5H Aug 2, 32 | 1020.2H 62.1M |  | 779.8H 177.9M |
| SERVO T/R (AC) / Ove 6700 | DUNLOP/ | AC67032 | CG107 | 24712 | 1800.0H 240.0M | 10817.0H Feb 6, 15 | 0.0H | 12617.0H Feb 6, 35 | 390.7H 32.0M |  | 1409.3H 208.0M |
| STARTER GENERATOR (900H) / Ove 8000 | / ASTAR | 150SG122Q | 52071 | 20950 | 900.0H | 10905.8H May 4, 15 |  | 11805.8H | 301.9H 29.1M |  | 598.1H |
| SURVIVAL KIT / Ins 2500 | I SERVICE CENTER/ | 6 PERSONNES / 5 JOURS | HI-TS-059 | 27826 | 12.0M* | 11187.8H Jun 21, 17 * | * | Jun 21, 18 * | 19.9H 3.5M* | * | 8.5M* |
| TAIL GEAR BOX / Ove 652000 | / | 350A33-0200-05 | M626 |  | 3000.0H 288.0M | 9305.1H Feb 9, 08 | 117.9H | 12187.2H Feb 9, 32 | 2020.5H 115.9M |  | 979.5H 172.1M |
| TAIL ROTOR BLADE / Ret 6400 | AIRBUS HELICOPTER/ AS350 | 355A12-0040-14 | 15911 | 41144 | 4000.0H | 11187.8H Jul 28, 17 | 2387.4H 3.9 | 12800.4H | 2407.3H 6.2M |  | 1592.7H |
| -- - 2500-HR/72M (tail boom-to-fuselage junction) / Ins 0500 | / |  |  |  | 2500.0H 72.0M | 9883.7H Apr 4, 12 |  | 12383.7H Apr 4, 18 | 1324.0H 66.1M |  | 1176.0H 5.9M |
| -- - 5400-HR (fins) / Ins 0500 | / |  |  |  | 5400.0H | 9883.7H |  | 15283.7H | 1324.0H |  | 4076.0H |
| TRANSPONDER TEST / Bi- | / |  |  |  | 24.0M | 11083.7H Feb 24, 16 |  | Feb 24, 18 | 124.0H 19.4M |  | 4.6M |

" * " indicates that a Manual Next Due is set.

| Recurring AD's |
| --- |
| AD No. | Description | Type | Limit | Perf. | Due | TTSC | Rem. |
| 2009-0019 Airframe 6700 | AD - ATA 67 - Rotors Flight Control Collective Pitch Lever Locking Stud Inspection / Repair S/B Ref: ASB 05.0058. | Recur | 660.0H 24.0M | 11083.7H Feb 25, 16 | 11743.7H Feb 25, 18 | 124.0H 19.4M | 536.0H 4.6M |
| 2009-0039 Airframe 6400 | AD - ATA 64 - Tail Rotor - Tail Rotor Blades Skin - Inspection / Repair S/B Ref: ASB 05.00.40. T/R BLADE assy 17222 | Recur | 100.0H | 11187.8H Jul 28, 17 | 11287.8H | 19.9H 2.3M | 80.1H |
| 2010-0006 Airframe 0500 | AD - Time Limits / Maintenance Checks - Tail Rotor (TR) Pitch-Change Links - Inspection S/B Ref: AS350 ASB NO. 05.00.60. | Recur | 100.0H | 11187.8H Jul 28, 17 | 11287.8H | 19.9H 2.3M | 80.1H |
| 2011-0038-E Airframe 6500 | AD - Tail Rotor Drive Tail Gearbox (TGB) Control Lever Inspection /Rework / Replacement S/B Ref: 05.00.62, REVISION 2. Control lever TGB (B) MA2709 | Recur | 660.0H | 11083.7H Feb 25, 16 | 11743.7H | 124.0H 19.4M | 536.0H |
| 2012-0071 Airframe 7200 Tolerance ±0% | AD - Engine; Axial Compressor, Gas Generator Hollow Shaft and Rear Bearing; Identification / Inspection / Cleaning / Replacement S/B Ref: A292 72 0230 VERSION C DATED 29 FEBRUARY 2012. MO-3 GAS GENERATOR (#1) 4373 | Recur | 750.0H* | 11083.7H* May 28, 14 | 11586.6H* | 124.0H* 40.3M | 378.9H* |
| 2012-0257-E Airframe 6400 | AD - Tail Rotor Laminated Half-Bearings ; Inspection / Replacement S/B Ref: AS350 EASB NO. 05.00.71. | Recur | 100.0H | 11187.8H Jul 28, 17 | 11287.8H | 19.9H 2.3M | 80.1H |
| 2014-0076-E Airframe 5300 | AD - Fuselage ; Rear Structure Junction Frame Reinforcement Angles Inspection S/B Ref: AS350 05.00.70. | Recur | 165.0H | 11176.6H Aug 9, 16 | 11341.6H | 31.1H 13.9M | 133.9H |
| 2015-0094 Airframe 0500 Cycle Name : Landings | Main Rotor Drive - Cross-Bar - Inspection S/B Ref: REFER TO AD. | Recur | 4500.0H 60000.0C | 10936.3H Jun 18, 15 27836.0C | 15436.3H 87836.0C | 271.4H 27.6M 728.0C | 4228.6H 59272.0C |
| 2015-0195 Airframe 6500 | AD - Tail Rotor Drive Shaft Bearings - Inspection / Replacement : AIRBUS HELICOPTER (ASB) AS350-01.00.70.. | Recur | 165.0H | 11187.8H Jul 28, 17 | 11352.8H | 19.9H 2.3M | 145.1H |
| 84-064-037(B)R3 pt 1 Airframe 6400 | AD - TAIL ROTOR BLADE SPARS S/B Ref: 05-11R5. | Recur | 100.0H | 11187.8H Jul 28, 17 | 11287.8H | 19.9H 2.3M | 80.1H |
| ASB AS350-05.00.84 Rev. 0 Airframe 63 Cycle Name : Landings | TIME LIMITS - MAINTENANCE CHECKS - Main rotor Drive. | Recur | 4500.0H 60000.0C | 10936.3H Jun 18, 15 27836.0C | 15436.3H 87836.0C | 271.4H 27.6M 728.0C | 4228.6H 59272.0C |
| CF-2004-10R1 Airframe 29 | Eurocopter (Aerospatiale) AS 350 - Hydraulic Power SB Ref: 63.00.08 + 29-00-04. | Recur | 165.0H 13.0M | 11187.8H Jul 28, 17 | 11352.8H Aug 28, 18 | 19.9H 2.3M | 145.1H 10.7M |
| F-2004-055 Airframe 2900 | AD - EUROCOPTER AS 350 - REPLACEMENT OF HYDRAULIC FLUID S/B Ref: ASB 05.00.45. | Recur | 110.0H | 11187.8H Jul 28, 17 | 11297.8H | 19.9H 2.3M | 90.1H |
| SB 62.00.31 para 2E2 Airframe | Frequency adapter locking wire check. | Recur | 100.0H | 11187.8H Jul 28, 17 | 11287.8H | 19.9H 2.3M | 80.1H |
| SB AS350 05.00.59 R1 Airframe 5300 | FUSELAGE - Visual check for cracks in the lower Crossbeams of the YAW control - Bellcrank Support. | Recur | 110.0H | 11187.8H Jul 28, 17 | 11297.8H | 19.9H 2.3M | 90.1H |
| SB AS350 05.00.75 R0 Airframe | Check of the tensioning of the SKURKA (EX APC) starter-gen. damper system. | Recur | 600.0H | 11002.1H Aug 25, 15 | 11602.1H | 205.6H 25.4M | 394.4H |
| SB AS350 05.00.78 R0 Airframe | Check of splice & rivets. | Recur | 600.0H | 11002.1H Aug 25, 15 | 11602.1H | 205.6H 25.4M | 394.4H |
| SB AS350-05.00.67 R1 Airframe 05 | INSPECTION OF THE LONGITUDINAL BULKHEADS FOR CRACKS. | Recur | 165.0H | 11176.6H Aug 9, 16 | 11341.6H | 31.1H 13.9M | 133.9H |

" * " indicates that a Manual Next Due is set.

| Inspections |
| --- |
| Inspection | Limit | Perf. | Due | TTSC | Rem. |
| 100-HOUR/12-MONTH | 100.0H 12.0M | 11187.8H Jul 28, 17 | 11287.8H Jul 28, 18 | 19.9H 2.3M | 80.1H 9.7M |
| 1200-HOUR/48-MONTH | 1200.0H 48.0M | 11083.7H Feb 25, 16 | 12283.7H Feb 25, 20 | 124.0H 19.4M | 1076.0H 28.6M |
| 144-MONTH | 144.0M | 10389.2H Apr 4, 12 | Apr 4, 24 | 818.5H 66.1M | 77.9M |
| 3rd 100-HOUR | 300.0H | 11002.1H Aug 25, 15 | 11302.1H | 205.6H 25.4M | 94.4H |
| 600-HOUR/24-MONTH | 600.0H 24.0M | 11083.7H Feb 25, 16 | 11683.7H Feb 25, 18 | 124.0H 19.4M | 476.0H 4.6M |
| INDICATING SYSTEM, Oil temperature warning system, check | 2400.0H 72.0M | 9883.7H Apr 4, 12 | 12283.7H Apr 4, 18 | 1324.0H 66.1M | 1076.0H 5.9M |

" * " indicates that a Manual Next Due is set.