|  | HN_C-FONZ Detailed View Registration HN_C-FONZ Date Mar 29, 2016 Make EUROCOPTER TTAF 8188.7 Model AS350BA+ Serial No. 1400 Engine Time TSN/TSO Engine (#1) 6522.4 6522.4 | Actions 12M - 12M-Inspection 24M - 24M-Inspection Ann - Annual up-date Bi- - Bi-Annual Test Cap - Capacity test Ins - Inspection O/C - O/C OC - OC Ops - Ops check OTL - OTL Ove - Overhaul REM - REMOVE & INSPECT Rep - Replacement Ret - Retirement Ser - Service var - various |
| --- | --- | --- |

| Cycles values |
| --- |
| Cycle Name | Value | Cycle Name | Value | Cycle Name | Value | Cycle Name | Value |
| ENG. - (HOURS) | 6 522.4 | ENG_#1_NG | 9 975.8 | ENG_#1_NP | 16 771.15 | External loads | 33.0 |
| HOOK TIME - (hours) | 0.8 | Landings | 22 538.0 | TORQUE CYCLES | 22 571.0 |  |  |

| Components |
| --- |
| Component/Action | Make/Model | Part No. | Serial No. | Tracking No. | Limit | Perf. | Time at Inst. | Due | TTSC | TTSN | Rem. |
| A.A.I.R. / Ann | / |  |  |  | 12.0M | Jan 15, 16 |  | Jan 15, 17 | 2.5M |  | 9.5M |
| ANTI-VIBRATOR / Ins 6200 | AIRBUS HELICOPTER/ AS350 | 350A31-0033-06 | SD150 | 24441 | 3000.0H 72.0M | 8073.3H Nov 25, 14 | 0.0H | 11073.3H Nov 25, 20 | 115.4H 16.1M |  | 2884.6H 55.9M |
| BLADE M/R (#1) / Ret 6200 | / | 355A11-0030-02 |  |  | 20000.0H | 8132.4H Jul 24, 15 |  | 28132.4H | 56.3H 8.2M | 5081.9H | 13000H |
| BLADE M/R (#2) / Ret 6200 | / | 355A11-0030-02 |  |  | 20000.0H | 8132.4H Jul 24, 15 |  | 28132.4H | 56.3H 8.2M | 5081.9H | 13000H |
| BLADE M/R (#3) / Ret 6200 | / | 355A11-0030-02 |  |  | 20000.0H | 8132.4H Jul 24, 15 |  | 28132.4H | 56.3H 8.2M | 5081.9H | 13000H |
| BLADE PINS / O/C | / |  |  |  |  |  |  |  |  |  |  |
| -- BLADE pin (#1) / O/C | / | 350A31-1771-21 | M24779 |  |  | 7561.7H |  |  | 627.0H |  |  |
| -- BLADE pin (#2) / O/C | / | 350A31-1771-21 | M24697 |  |  | 7561.7H |  |  | 627.0H |  |  |
| -- BLADE pin (#3) / O/C | AIRBUS HELICOPTER/ AS350 | 350A31-1770-01 | M42299 | 11299 |  | 8073.3H Nov 25, 14 |  |  | 115.4H 16.1M |  |  |
| -- BLADE pin (#4) / O/C | AIRBUS HELICOPTER/ AS350 | 350A31-1770-01 | M43459 | 6055 |  | 8073.3H Nov 25, 14 |  |  | 115.4H 16.1M |  |  |
| -- BLADE pin (#5) / O/C | / | 350A31-1771-21 | M25532 |  |  | 0.0H |  |  | 8188.7H |  |  |
| -- BLADE pin (#6) / O/C | / | 350A31-1771-21 | M24756 |  |  | 7561.7H |  |  | 627.0H |  |  |
| CAPACITY DAMPER (#1) / Ret 7100 | / | 350A54-1091-00 |  |  | 5400.0H | 6680.9H Mar 12, 09 | 0.0H | 12080.9H | 1507.8H 84.6M |  | 3892.2H |
| CAPACITY DAMPER (#2) / Ret 7100 | / | 366A54-1088-00 |  |  | 5000.0H | 6680.9H Mar 12, 09 | 0.0H | 11680.9H | 1507.8H 84.6M |  | 3492.2H |
| COMMUNICATION/navigation / O/C | / |  |  |  |  |  |  |  |  |  |  |
| -- AUDIO CONTROLLER / | / |  |  |  |  |  |  |  |  |  |  |
| -- COMM AM (#2) / O/C 2300 | / |  |  |  |  |  |  |  |  |  |  |
| -- COMM AM assy (#1) / | / |  |  |  |  |  |  |  |  |  |  |
| -- COMM FM assy (#1) / | / |  |  |  |  |  |  |  |  |  |  |
| -- COMM FM assy (#2) / | / |  |  |  |  |  |  |  |  |  |  |
| -- ELT 406AF / 12M 2500 | KANNAD/ 406 AF-COMPACT | S1840501-01 | 2620138-0021 | 24682 | 12.0M | 8156.6H Sep 24, 15 | 0.0H 0.0 | Sep 24, 16 | 32.1H 6.2M |  | 5.8M |
| -- ENCODER / O/C 3400 | TRANS-CAL/ | SSD120-30N | N18505 | 17199 |  | 8173.0H Oct 20, 15 |  |  | 15.7H 5.3M |  |  |
| -- TRANSPONDER / O/C 3400 | / | 066-1062-00 | 132112 |  |  |  |  |  |  |  |  |
| -- VHF / GPS ...to comm am 1 / O/C 3400 | GARMIN/ GNC250 | 011-00082-00 | 82901427 | 19403 |  | 8073.3H Nov 25, 14 | 157.3H |  | 272.7H 16.1M | 706.8H |  |
| -- VHF COMM transc...to comm am 2 / O/C | BENDIX KING/ KY196A | 064-1054-30 | 1175 | 31947 |  | 8173.0H Oct 21, 15 |  |  | 15.7H 5.3M |  |  |
| COMPASS SWING / Ser 053000 | / |  |  |  | 12.0M | 8173.0H Oct 20, 15 |  | Oct 20, 16 | 15.7H 5.3M |  | 6.7M |
| CROSSBEAM / Ins | / | 350A38-1040-20 | BYGBJ |  | 3000.0H 72.0M | 7916.0H Jun 3, 13 | 0.0H | 10916.0H Jun 3, 19 | 272.7H 33.9M |  | 2727.3H 38.1M |
| Engine (#1) / OC 7100 **Linked AD: SB LT101-71-00-0251 R1, 2011-08-06, 2009-24-12, 2002-03-09R1, 2001-25-04, 2001-22-07, 2001-17-15, 96-12-27, 96-12-05, 95-16-04, 94-18-06, 93-13-11, 92-15-07, 86-10-04, SB LT101-71-00-0251 R2, LTS101-73-10-0275, LTS101-72-50-0258 R3 | HONEYWELL/ LTS101-600A-3A | 4-001-000-31 | LE-43499CE |  |  | 8073.3H | 6407.0H |  | 6522.4H | 6522.4H |  |
| -- 100-HR inspection (#1) / 0500 | / |  |  |  | 100.0H 12.0M | 8173.0H Oct 20, 15 |  | 8273.0H Oct 20, 16 | 15.7H 5.3M |  | 84.3H 6.7M |
| -- 3rd 100-HR inspection (#1) / 0500 | / |  |  |  | 300.0H | 8073.3H Nov 25, 14 |  | 8373.3H | 115.4H 16.1M |  | 184.6H |
| -- 600-HR inspection (#1) / 0500 | / |  |  |  | 600.0H | 8073.3H Nov 25, 14 |  | 8673.3H | 115.4H 16.1M |  | 484.6H |
| -- A.G.B. MODULE (#1) / Ins 7260 **Linked AD: SB LTS 101-72-60-0211 R2 | / | 4-081-000-57 | W82J018 |  | 1800.0H | 8073.3H Feb 14, 14 | 339.1H | 9534.2H | 454.5H 25.5M | 9244.1H | 1345.5H |
| -- AIRFLOW MODULATOR (#1) / Ove 7500 | / | 4-301-102-12 | 15495 |  | 2400.0H | 8073.3H | 1363.4H | 9109.9H | 1478.8H |  | 921.2H |
| -- ENGINE OIL (Mobil 254) (#1) / Rep 7900 | / | MOBIL254 |  |  | 100.0H | 8173.0H Oct 20, 15 |  | 8273.0H | 15.7H 5.3M |  | 84.3H |
| -- ENGINE OIL filter (#1) / REM 7900 | / | 4-301-106-04 | 90293 | 33847 | 100.0H | 8188.7H Mar 14, 16 |  | 8288.7H | 0.0H 0.5M |  | 100.0H |
| -- FUEL CONTROL UNIT (#1) / Ove 7300 **Linked AD: SB LTS101-73-20-0272 R2 | HONEYWELL/ 2549165-1H+X | 4-301-288-06 | 50210 | 23489 | 2400.0H | 8132.4H Jul 24, 15 | 1194.6H | 9337.8H | 1250.9H 8.2M |  | 1149.1H |
| -- FUEL FILTER impending bypass indicator (#1) / Ops 0500 | / |  |  |  | 600.0H 12.0M | 8173.0H Oct 20, 15 |  | 8773.0H Oct 20, 16 | 15.7H 5.3M |  | 584.3H 6.7M |
| -- FUEL MANIFOLD, flex. (#1) / Ins 7300 | / | 4-191-100-03 | 11-169016-01964 |  | 1800.0H | 8073.3H | 104.4H | 9768.9H | 219.8H |  | 1580.2H |
| -- FUEL PUMP - (600-hr) (#1) / Ove 7300 | / | 4-301-377-01 | 0AFP826 |  | 2400.0H | 8073.3H | 104.4H | 10368.9H | 219.8H |  | 2180.2H |
| -- G.P. MODULE (#1) / Ins 7240 **Linked AD: SB LT101-72-30-0273 | / | 4-101-000-44 | W81K035 |  | 1800.0H | 8073.3H | 339.1H | 9534.2H | 454.5H |  | 1345.5H |
| -- HP FUEL FILTER (#1) / Rep | PUROLATOR/ LTS101 | 038072-18 |  | 19125 | 600.0H 24.0M | 8073.3H Nov 25, 14 |  | 8673.3H Nov 25, 16 | 115.4H 16.1M |  | 484.6H 7.9M |
| -- OIL PUMP - (ENGINE) (#1) / Ins 7900 | / | 4-301-243-02 | B-456 |  | 1800.0H | 8073.3H | 1272.5H | 8600.8H | 1387.9H | 4968.4H | 412.1H |
| -- OVERSPEED LIMITER (#1) / Ove 7600 | / | 4-301-235-07 | 28274 |  | 1400.0H | 8073.3H | 0.0H | 9473.3H | 115.4H |  | 1284.6H |
| -- P.T GOVERNOR (#1) / Ove 7300 **Linked AD: 2011-23-13, SB LTS101-73-20-A0268 R2 | / | 4-301-289-05 | 31107 |  | 2400.0H | 8073.3H Dec 9, 14 | 37.9H | 10435.4H | 153.3H 15.7M |  | 2246.7H |
| -- P.T. MODULE (#1) / Ins 7250 **Linked AD: SB LTS 101-79-20-0248 R2 | / | 4-141-000-78 | W81K035 |  | 1800.0H | 8073.3H | 339.1H | 9534.2H | 454.5H | 7875.4H | 1345.5H |
| -- T1 SENSOR (#1) / Ove 7700 | / | 4-301-099-07 | 16793 |  | 2400.0H | 8073.3H | 1294.5H | 9178.8H | 1409.9H |  | 990.1H |
| ENGINE TO M.G.B. COUPLING ASSY / O/C 6300 | / |  |  |  |  |  |  |  |  |  |  |
| EPICYCLIC (3000-HR) / Ove 6320 | / | 350A32-0100-10 |  |  | 3000.0H 288.0M | 8073.3H Apr 15, 14 |  | 11073.3H Apr 15, 38 | 115.4H 23.5M | 4086.0H | 1600H 222.5M |
| FIRE EXTINGUISHER (SLL=120M) / Ret 2600 | / | A1600 |  | 24998 | 120.0M | 8073.3H Dec 31, 14 |  | Dec 31, 24 | 115.4H 14.9M |  | 105.1M |
| FIRST AID KIT / Ins 2500 | / | PS-KIT | HI-PS-61 | 33732 | 12.0M* | 8173.0H Oct 20, 15 * | 0.0H 0.0 * | Oct 16, 16 * | 15.7H 5.3M* | * | 6.6M* |
| FUEL BOOST PUMP / Ins 2800 | / | P94B12-208 | 27919 |  | 2400.0H | 7999.2H | 0.0H | 10399.2H | 189.5H |  | 2210.5H |
| FUEL FILTER ELEMENT,A/F / Ret 2800 | PUROLATOR/ | 1763440 | 7363718821 | 25030 | 600.0H 24.0M | 8073.3H Nov 25, 14 |  | 8673.3H Nov 25, 16 | 115.4H 16.1M |  | 484.6H 7.9M |
| FUEL TANK / O/C | / |  |  |  |  |  |  |  |  |  |  |
| HOSES (RUBBER/POLYAMIDE, all) / Ret | / | RUBBER/POLYAMIDE |  |  | 144.0M | 8073.3H Nov 25, 14 |  | Nov 25, 26 | 115.4H 16.1M |  | 127.9M |
| HYD. OIL FILTER (p/n 157152) / Ret 2900 | / | 157152 |  |  | 1200.0H 48.0M | 7916.0H May 18, 13 | 0.0H | 9116.0H May 18, 17 | 272.7H 34.4M |  | 927.3H 13.6M |
| HYDRAULIC BELT / Ret 2900 | / | POLYV597K4 |  |  | 1800.0H 72.0M | 7556.0H Feb 24, 12 | 0.0H | 9356.0H Feb 24, 18 | 632.7H 49.2M |  | 1167.3H 22.8M |
| HYDRAULIC HOSES (074239) / | / |  |  |  |  |  |  |  |  |  |  |
| -- HYDRAULIC HOSE (A) / O/C 2900 | AIRBUS HELICOPTER/ AS350 | 704A34-412-255 | L201414582 | 25565 |  | 8073.3H Nov 25, 14 |  |  | 115.4H 16.1M |  |  |
| -- HYDRAULIC HOSE (B) / O/C 2900 | AIRBUS HELICOPTER/ AS350 | 704A34-412-255 | L2011304853 | 21876 |  | 8073.3H Nov 25, 14 |  |  | 115.4H 16.1M |  |  |
| -- HYDRAULIC HOSE (C) / O/C 2900 | AIRBUS HELICOPTER TEXTRON/ | 704A34412252 | L201401602 | 19573 | * | 8073.3H Nov 25, 14 * | * | Apr 30, 24 * | 115.4H 16.1M* | * | 97.0M* |
| -- HYDRAULIC HOSE (D) / O/C 2900 | AIRBUS HELICOPTER TEXTRON/ | 704A34412256 | L201407465 | 20157 | * | 8073.3H Nov 25, 14 * | * | Oct 31, 23 * | 115.4H 16.1M* | * | 91.1M* |
| HYDRAULIC HOSES (074686) / | / |  |  |  |  |  |  |  |  |  |  |
| -- HYDRAULIC HOSE (1) / O/C 2900 | / | 630B060076 |  | 22361 |  | 8073.3H Nov 25, 14 |  |  | 115.4H 16.1M |  |  |
| -- HYDRAULIC HOSE (2) / O/C 2900 | / | 630B060076 |  | 22361 |  | 8073.3H Nov 25, 14 |  |  | 115.4H 16.1M |  |  |
| -- HYDRAULIC HOSE (3) / O/C 2900 | / | 630B060076 | L201402801 | 18455 |  | 8073.3H Nov 25, 14 |  |  | 115.4H 16.1M |  |  |
| -- HYDRAULIC HOSE (4) / O/C 2900 | AIRBUS HELICOPTER/ | 630B080045 |  | 24206 |  | 8073.3H Nov 25, 14 |  |  | 115.4H 16.1M |  |  |
| -- HYDRAULIC HOSE (5) / O/C 2900 | AIRBUS HELICOPTER/ | 630B060078 | L201314320 | 17997 |  | 8073.3H Nov 25, 14 |  |  | 115.4H 16.1M |  |  |
| -- HYDRAULIC HOSE (6) / O/C 2900 | AIRBUS HELICOPTER/ | 630B060156 | L201314299 | 24207 |  | 8073.3H Nov 25, 14 |  |  | 115.4H 16.1M |  |  |
| HYDRAULIC OIL / Ret 2900 | / | ROYCO 782,MIL- PRF-83282 |  |  | 600.0H | 8073.3H | 0.0H | 8673.3H | 115.4H |  | 484.6H |
| HYDRAULIC PUMP / O/C 2900 | EUROCOPTER/ AS350 | 704A34-3100-06 | 10928669 | 17772 |  | 8073.3H Nov 25, 14 |  |  | 115.4H 16.1M |  |  |
| HYDRAULIC PUMP DRIVE assy / OC 2900 | AIRBUS HELICOPTERS/ AS350D,BA,B2 | 350A35-0131-00 |  |  |  |  |  |  |  |  |  |
| INSTRUMENTS / var various | / |  |  |  |  |  |  |  |  |  |  |
| -- ALTIMETRE / 24M 3400 | UNITED INSTRUMENT/ | 5934P-3 | 462327 | 23939 | 24.0M | 8073.3H Sep 29, 14 |  | Sep 29, 16 | 115.4H 18.0M |  | 6.0M |
| -- ATTITUDE GYRO ind. / O/C 3400 | / | 5040017908 | 25095 |  |  | 7575.2H Apr 21, 12 | 683.9H |  | 1297.4H 47.3M | 1297.4H |  |
| -- CARGO HOOK, load ind. / 2500 | / |  |  |  |  |  |  |  |  |  |  |
| -- CAUTION WARNING panel / O/C 3100 | / |  |  |  |  |  |  |  |  |  |  |
| -- CHRONO/CLOCK / O/C 3400 | / |  |  |  |  |  |  |  |  |  |  |
| -- COMPASS ind. / O/C 3400 | SIRS NAVIGATION/ | 1007KCA1 | BF9290411 | 8260 |  | 8073.3H Nov 25, 14 |  |  | 115.4H 16.1M |  |  |
| -- DIRECTIONAL GYRO ind. / O/C 3400 | / | 505-0010-902 |  |  |  |  |  |  |  |  |  |
| -- ENGINE instruments / O/C | / |  |  |  |  |  |  |  |  |  |  |
| -- FUEL QUANTITY ind. / O/C | / |  |  |  |  |  |  |  |  |  |  |
| -- MULTIPLE INSTRUMENT ind. / O/C | / |  |  |  |  |  |  |  |  |  |  |
| -- NR ind. / O/C 6200 | / | 6503-1032 | 107 | 18712 |  | 8073.3H Nov 25, 14 |  |  | 115.4H 16.1M |  |  |
| -- VERTICAL SPEED ind. / O/C 3400 | UNITED INSTRUMENT/ | 7000 | 6950 | 13153 |  | 8073.3H Nov 25, 14 |  |  | 115.4H 16.1M |  |  |
| -- VOLTMETER / O/C 2400 | / |  |  |  |  |  |  |  |  |  |  |
| LANDING GEAR SHOCK ABSORBER (#1) / Ins | AIRBUS HELICOPTER/ | 350A75-2096-00 |  | 22475 | 5400.0H | 8073.3H Nov 25, 14 |  | 13473.3H | 115.4H 16.1M |  | 5284.6H |
| LANDING GEAR SHOCK ABSORBER (#2) / Ins | AIRBUS HELICOPTER/ | 350A75-2096-00 | AFF200909 | 22172 | 5400.0H | 8073.3H Nov 25, 14 |  | 13473.3H | 115.4H 16.1M |  | 5284.6H |
| MAIN ROTOR HEAD ASSY / O/C 622000 | AIRBUS HELICOPTERS/ AS350 | 350A31-0000-01 | M367 | 26282 |  | Nov 25, 14 |  |  | 16.1M |  |  |
| -- BLADE HORN (#1) / Ret 622000 | / | 350A31-1877-02 | M112031 |  | 80000.0H | 8073.3H Nov 25, 14 | 3728.9H | 84344.4H | 3844.3H 16.1M |  | 76155.7H |
| -- BLADE HORN (#2) / Ret 622000 | / | 350A31-1877-02 | M1574 |  | 80000.0H | 8073.3H Nov 25, 14 | 3728.9H | 84344.4H | 3844.3H 16.1M |  | 76155.7H |
| -- BLADE HORN (#3) / Ret 622000 | / | 350A31-1877-02 | M111563 |  | 80000.0H | 8073.3H Nov 25, 14 | 3728.9H | 84344.4H | 3844.3H 16.1M |  | 76155.7H |
| -- FREQUENCY ADAPTER (#1) / O/C 6200 | / | 365A31-1019-23 | 11072 |  |  | Nov 25, 14 |  |  | 16.1M |  |  |
| -- FREQUENCY ADAPTER (#2) / O/C 6200 | / | 365A31-1019-23 | 11079 |  |  | Nov 25, 14 |  |  | 16.1M |  |  |
| -- FREQUENCY ADAPTER (#3) / O/C 6200 | / | 365A31-1019-23 | 11077 |  |  | Nov 25, 14 |  |  | 16.1M |  |  |
| -- SLEEVE LOWER FLANGE (#1) / Ret 622000 | / | 350A31-1850-02 | M6498 |  | 4400.0H | 8073.3H Nov 25, 14 | 2250.8H | 10222.5H | 2366.2H 16.1M |  | 2033.8H |
| -- SLEEVE LOWER FLANGE (#2) / Ret 622000 | / | 350A31-1850-02 | M6428 |  | 4400.0H | 8073.3H Nov 25, 14 | 2250.8H | 10222.5H | 2366.2H 16.1M |  | 2033.8H |
| -- SLEEVE LOWER FLANGE (#3) / Ret 622000 | / | 350A31-1850-02 | M6426 |  | 4400.0H | 8073.3H Nov 25, 14 | 2250.8H | 10222.5H | 2366.2H 16.1M |  | 2033.8H |
| -- SLEEVE UPPER FLANGE (#1) / Ret 622000 | / | 350A31-1850-03 | M6517 |  | 4400.0H | 8073.3H Nov 25, 14 | 2250.8H | 10222.5H | 2366.2H 16.1M |  | 2033.8H |
| -- SLEEVE UPPER FLANGE (#2) / Ret 622000 | / | 350A31-1850-03 | M6499 |  | 4400.0H | 8073.3H Nov 25, 14 | 2250.8H | 10222.5H | 2366.2H 16.1M |  | 2033.8H |
| -- SLEEVE UPPER FLANGE (#3) / Ret 622000 | / | 350A31-1850-03 | M6500 |  | 4400.0H | 8073.3H Nov 25, 14 | 2250.8H | 10222.5H | 2366.2H 16.1M |  | 2033.8H |
| -- SPH THRUST bearing (#1) / Ret 622000 | / | 704A33-633-20851 | LK12747 |  | 6400.0H | 8073.3H Nov 25, 14 | 1742.6H | 12730.7H | 1858.0H 16.1M | 1858.0H | 4542.0H |
| -- SPH THRUST bearing (#2) / Ret 622000 | / | 704A33-633-20851 | LK12795 |  | 6400.0H | 8073.3H Nov 25, 14 | 1742.6H | 12730.7H | 1858.0H 16.1M | 1858.0H | 4542.0H |
| -- SPH THRUST bearing (#3) / Ret 622000 | / | 704A33-633-20851 | LK12813 |  | 6400.0H | 8073.3H Nov 25, 14 | 1742.6H | 12730.7H | 1858.0H 16.1M | 1858.0H | 4542.0H |
| -- SPH THRUST BRG BOLT (#1) / Ret 622000 | / | 350A31-1854-21 | 12077 |  | 3000.0H | 8073.3H Nov 25, 14 | 2250.8H | 8822.5H | 2366.2H 16.1M |  | 633.8H |
| -- SPH THRUST BRG BOLT (#2) / Ret 622000 | / | 350A31-1854-21 | 12150 |  | 3000.0H | 8073.3H Nov 25, 14 | 2250.8H | 8822.5H | 2366.2H 16.1M |  | 633.8H |
| -- SPH THRUST BRG BOLT (#3) / Ret 622000 | / | 350A31-1854-21 | 12156 |  | 3000.0H | 8073.3H Nov 25, 14 | 2250.8H | 8822.5H | 2366.2H 16.1M |  | 633.8H |
| -- SPH THRUST BRG BOLT (#4) / Ret 622000 | / | 350A31-1854-21 | 12102 |  | 3000.0H | 8073.3H Nov 25, 14 | 2250.8H | 8822.5H | 2366.2H 16.1M |  | 633.8H |
| -- SPH THRUST BRG BOLT (#5) / Ret 622000 | / | 350A31-1854-21 | 12087 |  | 3000.0H | 8073.3H Nov 25, 14 | 2250.8H | 8822.5H | 2366.2H 16.1M |  | 633.8H |
| -- SPH THRUST BRG BOLT (#6) / Ret 622000 | / | 350A31-1854-21 | 12162 |  | 3000.0H | 8073.3H Nov 25, 14 | 2250.8H | 8822.5H | 2366.2H 16.1M |  | 633.8H |
| -- STARFLEX / Ret 622000 | / | 350A31-1917-00 | M1605 |  | 2400.0H | 8073.3H Nov 25, 14 | 1742.6H | 8730.7H | 1858.0H 16.1M | 1858.0H | 542.0H |
| MAIN ROTOR MAST ASSY / O/C 623000 | / | 350A37-0003-05 | M1335 | 17756 |  | Nov 25, 14 |  |  | 16.1M |  |  |
| MGB BEVEL REDUCTION GEAR / Ove 6300 | / | 350A32-0300-05N | M2240 | 17768 | 3500.0H 288.0M | 8073.3H Dec 7, 10 | 991.3H | 10582.0H Dec 7, 34 | 1106.7H 63.7M | 7917.1H | 2393.3H 224.3M |
| MRH ATTACHMENT BOLTS / 623000 | / |  |  |  |  |  |  |  |  |  |  |
| -- MRH attachment bolt (#1) / Ret 623000 | / | 350A37-1244-20 | 80392 |  | 3000.0H | 8073.3H Feb 28, 14 | 517.3H | 10556.0H | 632.7H 25.0M |  | 2367.3H |
| -- MRH attachment bolt (#2) / Ret 623000 | / | 350A37-1244-20 | 80837 |  | 3000.0H | 8073.3H Feb 28, 14 | 517.3H | 10556.0H | 632.7H 25.0M |  | 2367.3H |
| -- MRH attachment bolt (#3) / Ret 623000 | / | 350A37-1244-20 | 80879 |  | 3000.0H | 8073.3H Feb 28, 14 | 517.3H | 10556.0H | 632.7H 25.0M |  | 2367.3H |
| -- MRH attachment bolt (#4) / Ret 623000 | / | 350A37-1244-020 | 80118 |  | 3000.0H | 8073.3H Feb 28, 14 | 517.3H | 10556.0H | 632.7H 25.0M |  | 2367.3H |
| -- MRH attachment bolt (#5) / Ret 623000 | / | 350A37-1244-20 | 80940 |  | 3000.0H | 8073.3H Feb 28, 14 | 517.3H | 10556.0H | 632.7H 25.0M |  | 2367.3H |
| -- MRH attachment bolt (#6) / Ret 623000 | / | 350A37-1244-20 | 80136 |  | 3000.0H | 8073.3H Feb 28, 14 | 517.3H | 10556.0H | 632.7H 25.0M |  | 2367.3H |
| -- MRH attachment bolt (#A) / Ret 623000 | / | 350A37-1245-20 | 74806 |  | 3000.0H | 8073.3H Feb 28, 14 | 517.3H | 10556.0H | 632.7H 25.0M |  | 2367.3H |
| -- MRH attachment bolt (#B) / Ret 623000 | / | 350A37-1245-20 | 74856 |  | 3000.0H | 8073.3H Feb 28, 14 | 517.3H | 10556.0H | 632.7H 25.0M |  | 2367.3H |
| -- MRH attachment bolt (#C) / Ret 623000 | / | 350A37-1245-20 | 74852 |  | 3000.0H | 8073.3H Feb 28, 14 | 517.3H | 10556.0H | 632.7H 25.0M |  | 2367.3H |
| -- MRH attachment bolt (#D) / Ret 623000 | / | 350A37-1245-20 | 74829 |  | 3000.0H | 8073.3H Feb 28, 14 | 517.3H | 10556.0H | 632.7H 25.0M |  | 2367.3H |
| -- MRH attachment bolt (#E) / Ret 623000 | / | 350A37-1245-20 | 74673 |  | 3000.0H | 8073.3H Feb 28, 14 | 517.3H | 10556.0H | 632.7H 25.0M |  | 2367.3H |
| -- MRH attachment bolt (#F) / Ret 623000 | / | 350A37-1245-20 | 75264 |  | 3000.0H | 8073.3H Feb 28, 14 | 517.3H | 10556.0H | 632.7H 25.0M |  | 2367.3H |
| OIL PUMP, MGB (post mod 07-7175) / Ove 6300 | / | 350A32-0400-00 | M2351 | 17752 | 3500.0H 288.0M | 8073.3H Nov 25, 14 | 991.3H | 10582.0H Nov 25, 38 | 1106.7H 16.1M | 7917.1H | 2393.3H 271.9M |
| OPTIONAL equipment / var | / |  |  |  |  |  |  |  |  |  |  |
| SEAT BELT, LAP (co-PILOT) / OTL 2500 | / | AFG0348026 | 503761-497 |  | 120.0M | Apr 30, 09 |  | Apr 30, 19 | 83.0M |  | 37.0M |
| SEAT BELT, LAP (PILOT) / OTL 2500 | / | AFG0348031 | AS350-159 | 24201 | 120.0M | 8073.3H Sep 8, 14 |  | Sep 8, 24 | 115.4H 18.7M |  | 101.3M |
| SEAT BELT, LAP, AFT (L/H CTR) / OTL 2500 | / | G10601-4 | GEN-350-163 |  | 120.0M | Nov 2, 11 |  | Nov 2, 21 | 52.9M |  | 67.1M |
| SEAT BELT, LAP, AFT (L/H) / OTL 2500 | / | G10601-4 | GEN-350-164 |  | 120.0M | Nov 2, 11 |  | Nov 2, 21 | 52.9M |  | 67.1M |
| SEAT BELT, LAP, AFT (R/H CTR) / OTL 2500 | / | G10601-4 | GEN-350-165 |  | 120.0M | Nov 2, 11 |  | Nov 2, 21 | 52.9M |  | 67.1M |
| SEAT BELT, LAP, AFT (R/H) / OTL 2500 | / | G10601-4 | GEN-350-166 |  | 120.0M | Nov 2, 11 |  | Nov 2, 21 | 52.9M |  | 67.1M |
| SERVO M/R (SC) (#1) / Ove 6700 | GOODRICH/ SAMM | SC5084 | 205M | 17769 | 3000.0H 240.0M | 8073.3H Jul 11, 12 | 368.2H | 10705.1H Jul 11, 32 | 483.6H 44.6M | 4154.9H | 1250H 195.4M |
| SERVO M/R (SC) (#2) / Ove 6700 | / SAMM | SC5083 | 1305 | 17770 | 3000.0H 240.0M | 8073.3H Feb 22, 11 | 1967.6H | 9105.7H Feb 22, 31 | 2083.0H 61.2M | 5058.7H | 917H 178.8M |
| SERVO M/R (SC) (#3) / Ove 6700 | / SAMM | SC5083 | 315 | 17771 | 3000.0H 240.0M | 8073.3H Mar 17, 08 | 1128.2H | 9945.1H Mar 17, 28 | 1243.6H 96.4M | 4370.6H | 1756H 143.6M |
| SERVO T/R (AC) / Ove 6700 | / DUNLOP | AC67032 | LY 018 |  | 1800.0H 240.0M | 6459.2H Aug 31, 07 | 0.0H | 8259.2H Aug 31, 27 | 1729.5H 102.9M | 7303.1H | 70.5H 137.1M |
| SHLD HARN ASSY (co-PILOT) / OTL 2500 | / | 504084-401-7497 | AS350-209 |  | 120.0M | Apr 11, 11 |  | Apr 11, 21 | 59.6M |  | 60.4M |
| SHLD HARN ASSY (PILOT) / OTL 2500 | / | AFG0582730 | 5477 |  | 120.0M | Sep 18, 12 |  | Sep 18, 22 | 42.4M |  | 77.6M |
| SHLD HARN ASSY, AFT (L/H CTR) / OTL 2500 | / | G10601-2 | SAME-AS--SEAT-BELT |  | 120.0M | Nov 2, 14 |  | Nov 2, 24 | 16.9M |  | 103.1M |
| SHLD HARN ASSY, AFT (L/H) / OTL 2500 | / | G10601-2 | SAME-AS--SEAT-BELT |  | 120.0M | Nov 2, 14 |  | Nov 2, 24 | 16.9M |  | 103.1M |
| SHLD HARN ASSY, AFT (R/H CTR) / OTL 2500 | / | G10601-2 | SAME-AS--SEAT-BELT |  | 120.0M | Nov 2, 14 |  | Nov 2, 24 | 16.9M |  | 103.1M |
| SHLD HARN ASSY, AFT (R/H) / OTL 2500 | / | G10601-2 | SAME-AS--SEAT-BELT |  | 120.0M | Nov 2, 14 |  | Nov 2, 24 | 16.9M |  | 103.1M |
| STARTER GENERATOR / Ove 8000 | / | 23032-027 | 15149 |  | 1200.0H | 7433.3H | 0.0H | 8633.3H | 755.4H |  | 444.6H |
| SURVIVAL KIT / Ins 2500 | / 6 PERSONNES 5 JOURS | SURVIVAL KIT | HI-TS-063 | 20595 | 12.0M | 8134.0H Jun 2, 15 |  | Jun 2, 16 | 54.7H 9.9M |  | 2.1M |
| SUSPENSION BARS, MGB / 6300 | / |  |  |  |  |  |  |  |  |  |  |
| -- SUSPENSION BAR, MGB (#1) (AFT) / O/C 6300 | / |  |  |  |  |  |  |  |  |  |  |
| -- SUSPENSION BAR, MGB (#1) (FWD) / O/C 6300 | / |  |  |  |  |  |  |  |  |  |  |
| -- SUSPENSION BAR, MGB (#2) (AFT) / O/C 6300 | / |  |  |  |  |  |  |  |  |  |  |
| -- SUSPENSION BAR, MGB (#2) (FWD) / O/C 6300 | / | 704A33-633-074 |  |  |  |  |  |  |  |  |  |
| SUSPENSION SYSTEM / 2500 | / |  |  |  |  |  |  |  |  |  |  |
| -- CARGO HOOK / Ove 2500 Cycle Name : HOOK TIME - (hours) | ONBOARD SYSTEMS/ | 528-023-01 | 270 | 12834 | 60.0M 1000.0C | 8073.3H Nov 25, 14 0.0C | 0.0C | Nov 25, 19 1000.0C | 115.4H 16.1M 0.8C |  | 43.9M 999.2C |
| -- CARGO SLING / 2500 | / |  |  |  |  |  |  |  |  |  |  |
| T/R D/S FRONT SECTION / O/C 6500 | / |  |  |  |  |  |  |  |  |  |  |
| T/R D/S REAR SECTION / O/C 6500 | / | 350A34-0110-05 | U/K | 33949 |  | 8173.0H Oct 20, 15 |  |  | 15.7H 5.3M |  |  |
| T/R HUB ASSY / O/C 6400 | / |  |  |  |  |  |  |  |  |  |  |
| T/R SPIDER assy / O/C 6500 | / | 350A33-2030-00 | M1545 |  |  | 5498.9H |  |  | 2689.8H | 10093.3H |  |
| TAIL ROTOR BLADE / Ret 6400 | / | 355A12-0040-14 | 15991 |  | 4000.0H | 6811.6H | 0.0H | 10811.6H | 1377.1H |  | 1622H |
| TAILBOOM assy / OC 5300 | / |  |  |  |  |  |  |  |  |  |  |
| -- TAILBOOM / OC 5300 | / | 350A23-0000-0101 |  |  |  |  |  |  |  |  |  |
| -- VERTICAL FIN, lower / OC 5500 | / | 350A14-0020-0602 |  |  |  |  |  |  |  |  |  |
| -- VERTICAL FIN, upper / OC 5500 | / | 350A14-0021-0401 |  |  |  |  |  |  |  |  |  |
| TAILBOOM to fuselage / Ins 0500 | / |  |  |  | 2500.0H 72.0M | 8073.3H Nov 25, 14 |  | 10573.3H Nov 25, 20 | 115.4H 16.1M |  | 2384.6H 55.9M |
| TGB ASSY / Ove 652000 | / | 350A33-0200-05 | MA0311 |  | 3000.0H 288.0M | 7259.9H May 25, 11 | 0.0H | 10259.9H May 25, 35 | 928.8H 58.1M | 7062.4H | 2071.2H 229.9M |
| THRU SHAFT (ENGINE) / Ins 6300 | / | 350A35-1001-22 | 06L1J |  | 600.0H | 8073.3H Nov 25, 14 |  | 8673.3H | 115.4H 16.1M |  | 484.6H |
| TRANSPONDER TEST / Bi- 2300 | / |  |  |  | 24.0M | Nov 17, 14 |  | Nov 17, 16 | 16.4M |  | 7.6M |

" * " indicates that a Manual Next Due is set.

| Recurring AD's |
| --- |
| AD No. | Description | Type | Limit | Perf. | Due | TTSC | Rem. |
| 2009-0019 Airframe 6700 Tolerance ±0% | AD - ATA 67 - Rotors Flight Control Collective Pitch Lever Locking Stud Inspection / Repair S/B Ref: ASB 05.0058. | Recur | 660.0H 24.0M | 8075.8H Dec 17, 14 | 8735.8H Dec 17, 16 | 112.9H 15.4M | 547.1H 8.6M |
| 2009-0039 Airframe 6400 Tolerance ±0% | AD - ATA 64 - Tail Rotor - Tail Rotor Blades Skin - Inspection / Repair S/B Ref: ASB 05.00.40. T/R BLADE assy 15991 | Recur | 100.0H | 8173.0H Oct 20, 15 | 8273.0H | 15.7H 5.3M | 84.3H |
| 2010-0006 Airframe 0500 Tolerance ±0% | AD - Time Limits / Maintenance Checks - Tail Rotor (TR) Pitch-Change Links - Inspection S/B Ref: AS350 ASB NO. 05.00.60. | Recur | 100.0H | 8173.0H Oct 20, 15 | 8273.0H | 15.7H 5.3M | 84.3H |
| 2011-0038-E Airframe 6500 Tolerance ±0% | AD - Tail Rotor Drive Tail Gearbox (TGB) Control Lever Inspection /Rework / Replacement S/B Ref: 05.00.62, REVISION 2. Control lever TGB (B) MA04887 | Recur | 660.0H | 7840.6H Apr 30, 13 | 8500.6H | 348.1H 35.0M | 311.9H |
| 2011-23-13 Engine | Power turbine governor S/B Ref: HONEYWELL SB LTS101-73-20-A0268. P.T GOVERNOR (#1) 31107 | Recur | 900.0H* | * | 8935.4H* | * | 746.7H* |
| 2012-0257-E Airframe 6400 Tolerance ±0% | AD - Tail Rotor Laminated Half-Bearings Inspection / Replacement S/B Ref: AS350 EASB NO. 05.00.71. | Recur | 100.0H | 8173.0H Oct 20, 15 | 8273.0H | 15.7H 5.3M | 84.3H |
| 2013-0133 Airframe 6400 Tolerance ±0% | AD - Tail Rotor Tail Rotor Hub Pitch Horn Inspection / Replacement S/B Ref: ASB NO. 05.00.74 ORIGINAL ISSUE DATED 27 MAY 2013, OR REV. 1 DATED 25 JUNE 2013.. | Recur | 110.0H | 8173.0H Oct 20, 15 | 8283.0H | 15.7H 5.3M | 94.3H |
| 2015-0094 Airframe Cycle Name : Landings | Main Rotor Drive - Cross-Bar - Inspection S/B Ref: REFER TO AD. | Recur | 4500.0H 60000.0C | 8103.3H Jun 18, 15 22441.0C | 12603.3H 82441.0C | 85.4H 9.4M 97.0C | 4414.6H 59903.0C |
| 2015-0195 Airframe 6500 | AD - Tail Rotor Drive Shaft Bearings - Inspection / Replacement : AIRBUS HELICOPTER (ASB) AS350-01.00.70.. | Recur | 165.0H | 8073.3H Oct 19, 15 | 8238.3H | 115.4H 5.3M | 49.6H |
| 84-064-037(B) R3 Pt3 Airframe 6400 Tolerance ±0% | AD - TAIL ROTOR BLADE SPARS S/B Ref: 05-11R5. | Recur | 600.0H | 8073.3H Nov 25, 14 | 8673.3H | 115.4H 16.1M | 484.6H |
| 84-064-037(B)R3 Pt1 Airframe 6400 Tolerance ±0% | AD - TAIL ROTOR BLADE SPARS S/B Ref: 05-11R5. | Recur | 100.0H | 8173.0H Oct 20, 15 | 8273.0H | 15.7H 5.3M | 84.3H |
| 88-14-01 part B & F Engine 7200 Tolerance ±0% | AD - RBSH and full flow scavenge debris monitor indicator light continuity and metal contamination.. Engine LE-43499CE | Recur | 100.0H | 8173.0H Oct 20, 15 | 8273.0H | 15.7H 5.3M | 84.3H |
| 88-14-01 Pt D Engine 7200 | AD - # 3 + 4 BEARINGS / POWER TURBINE DISCS S/B Ref: 77-30-0104R1. Engine LE-43499CE | Recur | 100.0H | 8173.0H Oct 20, 15 | 8273.0H | 15.7H 5.3M | 84.3H |
| 88-14-01 pt G Engine 7200 | AD - Delta "P" check. Engine LE-43499CE | Recur | 100.0H | 8173.0H Oct 20, 15 | 8273.0H | 15.7H 5.3M | 84.3H |
| ASB AS350-05.00.84 Rev. 0 Airframe 63 Cycle Name : Landings | TIME LIMITS - MAINTENANCE CHECKS - Main rotor Drive. | Recur | 4500.0H 60000.0C | 8103.3H Jun 18, 15 22441.0C | 12603.3H 82441.0C | 85.4H 9.4M 97.0C | 4414.6H 59903.0C |
| CF-2004-10R1 Airframe 29 | Eurocopter (Aerospatiale) AS 350 - Hydraulic Power SB Ref: 63.00.08 + 29-00-04. | Recur | 165.0H 13.0M | 8188.7H Mar 14, 16 | 8353.7H Apr 14, 17 | 0.0H 0.5M | 165.0H 12.5M |
| F-2004-055 Airframe 2900 Tolerance ±0% | AD - EUROCOPTER AS 350 - REPLACEMENT OF HYDRAULIC FLUID S/B Ref: ASB 05.00.45. | Recur | 110.0H 1.0M | 8188.7H Mar 14, 16 | 8298.7H Apr 14, 16 | 0.0H 0.5M | 110.0H 0.5M |
| LTS101-72-50-0258 R3 Engine 7200 | ENGINE - TURBINE SECTION - Gas Generator Nozzle, part nos 4-111-090-12,4-111-090R22, 4-111-090R24, 4-111-090-25, 4-111-090-26 and 4-111-090-27 inspection.. Engine (#1) LE-43499CE | Recur | 1800.0H* | * | 9534.2H* | * | 1345.5H* |
| SB 62.00.31 R0 para 2E2 Airframe | FREQUENCY ADAPTER VENTILATION HOLES. | Recur | 100.0H | 8173.0H Oct 20, 15 | 8273.0H | 15.7H 5.3M | 84.3H |
| SB 63.00.17 R2, pt 2B1 & 2B3 Airframe | Check of the Hydraulic Pump Drive Pulley. | Recur | 110.0H | 8173.0H Oct 20, 15 | 8283.0H | 15.7H 5.3M | 94.3H |
| SB 63.00.17 R3, pt 2B1 & 2B3 Airframe | Main rotor drive - Check of the Hydraulic Pump Drive Pulley. | Recur | 110.0H | 8173.0H Oct 20, 15 | 8283.0H | 15.7H 5.3M | 94.3H |
| SB AS350 05.00.59 R1 Airframe 5300 | FUSELAGE - Visual check for cracks in the lower Crossbeam of the YAW control - Bellcrank Support. | Recur | 110.0H | 8173.0H Oct 20, 15 | 8283.0H | 15.7H 5.3M | 94.3H |
| SB AS350-05.00.75 R0 Airframe | ENGINE STARTING - Starter control - Periodic adjustment and check. | Recur | 600.0H | 8073.3H Nov 25, 14 | 8673.3H | 115.4H 16.1M | 484.6H |
| SB AS350-05.00.78 R0 Airframe | Fuselage bottom structure - Check of splices & Rivets. | Recur | 600.0H | 8073.3H Nov 25, 14 | 8673.3H | 115.4H 16.1M | 484.6H |
| SB LT101-71-00-0251 R2 Engine | Bearing Package Oil Jets (Delta-P Check) Inspection on LT101 Engines. Engine (#1) LE-43499CE | Recur | 100.0H | 8173.0H Oct 20, 15 | 8273.0H | 15.7H 5.3M | 84.3H |
| SB LTS101-73-20-0272 R2 Engine | ENGINE - FUEL SYSTEM - Repetitive replacement of spq= ×£pÍ¿. FUEL CONTROL UNIT (#1) 50210 | Recur | 600.0H* | * | 8730.7H* | * | 542.0H* |

" * " indicates that a Manual Next Due is set.

| Inspections |
| --- |
| Inspection | Limit | Perf. | Due | TTSC | Rem. |
| 100-HR | 100.0H 12.0M | 8173.0H Oct 20, 15 | 8273.0H Oct 20, 16 | 15.7H 5.3M | 84.3H 6.7M |
| 1200-HR/4Y | 1200.0H 48.0M | 8073.3H Nov 25, 14 | 9273.3H Nov 25, 18 | 115.4H 16.1M | 1084.6H 31.9M |
| 2400-HR/6Y | 2400.0H 72.0M | 8073.3H Nov 25, 14 | 10473.3H Nov 25, 20 | 115.4H 16.1M | 2284.6H 55.9M |
| 3000-HR/6Y | 3000.0H 72.0M | 8073.3H Nov 25, 14 | 11073.3H Nov 25, 20 | 115.4H 16.1M | 2884.6H 55.9M |
| 3rd 100-HR | 300.0H | 8073.3H Nov 25, 14 | 8373.3H | 115.4H 16.1M | 184.6H |
| 5400-HR | 5400.0H | 8073.3H Nov 25, 14 | 13473.3H | 115.4H 16.1M | 5284.6H |
| 600-HR/24M(T) | 600.0H 24.0M | 8073.3H Nov 25, 14 | 8673.3H Nov 25, 16 | 115.4H 16.1M | 484.6H 7.9M |
| Check FULL and LOW level light of capacitive and resistive gauges. | 600.0H* 24.0M* | * * | 8673.3H* Nov 25, 16 * | * * | 484.6H* 7.9M* |
| M/R BLADE PINS - lubrication | 200.0H 6.0M | 8173.0H Oct 20, 15 | 8373.0H Apr 20, 16 | 15.7H 5.3M | 184.3H 0.7M |
| MAJOR (C) | 144.0M | 8073.3H Nov 25, 14 | Nov 25, 26 | 115.4H 16.1M | 127.9M |
| MRR 32.10.11.751, LANDING GEAR SHOCK ABSORBER INSPECTION | 5400.0H | 8073.3H Nov 25, 14 | 13473.3H | 115.4H 16.1M | 5284.6H |
| POWER CHECK | 50.0H | 8188.7H Mar 14, 16 | 8238.7H | 0.0H 0.5M | 50.0H |

" * " indicates that a Manual Next Due is set.

| A.G.B. MODULE (#1) - Assembly - PN: 4-081-000-57 SN: W82J018 |
| --- |
| Component/Action | Make/Model | Part No. | Serial No. | Tracking No. | Limit | Perf. | Time at Inst. | Due | TTSC | TTSN | Rem. |
| A.G.B. MODULE (#1) / Ins 7260 **Linked AD: SB LTS 101-72-60-0211 R2 | / | 4-081-000-57 | W82J018 |  | 1800.0H | 8073.3H Feb 14, 14 | 339.1H | 9534.2H | 454.5H 25.5M | 9244.1H | 1345.5H |
| -- - #4 Bearing, AGB (#1) / O/C | / . | 4-301-306-03 | NSN |  |  | 8073.3H | 684.5H |  | 799.9H | 3182.5H |  |
| -- - #5 Bearing, AGB (#1) / O/C | / . | 4-301-306-03 | NSN |  |  | 8073.3H | 684.5H |  | 799.9H | 3182.5H |  |
| -- - Outpout gear, AGB (#1) / O/C | / . | 4-081-120-17 | 002524200023 |  |  | 8073.3H | 3485.1H |  | 3600.5H | 3261.4H |  |
| -- - power pinion gear, AGB (#1) / O/C | / . | 4-081-053-11 | 07-25174-00764 |  |  | 8073.3H | 684.5H |  | 799.9H | 3182.5H |  |
| -- - Torque idler gear, AGB (#1) / O/C | / . | 4-081-070-42 | 09-169034-00011 |  |  | 8073.3H | 339.1H |  | 454.5H |  |  |

" * " indicates that a Manual Next Due is set.

| ALTIMETRE - Assembly - PN: 5934P-3 SN: 462327 |
| --- |
| Component/Action | Make/Model | Part No. | Serial No. | Tracking No. | Limit | Perf. | Time at Inst. | Due | TTSC | TTSN | Rem. |
| ALTIMETRE / 24M 3400 | UNITED INSTRUMENT/ | 5934P-3 | 462327 | 23939 | 24.0M | 8073.3H Sep 29, 14 |  | Sep 29, 16 | 115.4H 18.0M |  | 6.0M |
| -- PITOT STATIC, leak check / Tes | / |  |  |  | 24.0M | Nov 17, 14 |  | Nov 17, 16 | 16.4M |  | 7.6M |

" * " indicates that a Manual Next Due is set.

| BLADE TIE-DOWN KIT (STC SH96-126) - Assembly - PN: 350-700414 |
| --- |
| Component/Action | Make/Model | Part No. | Serial No. | Tracking No. | Limit | Perf. | Time at Inst. | Due | TTSC | TTSN | Rem. |
| BLADE TIE-DOWN KIT (STC SH96-126) / 2500 | EUROCOPTER CANADA/ AS350/355 | 350-700414 |  |  |  |  |  |  |  |  |  |
| -- - 150-HR/12M (STC SH96-126) / Ins 0500 | / |  |  |  | 150.0H 12.0M | 8173.0H Oct 20, 15 |  | 8323.0H Oct 20, 16 | 15.7H 5.3M |  | 134.3H 6.7M |
| -- - 600-HR/24M (STC SH96-126) / Ins 0500 | / |  |  |  | 600.0H* 24.0M* | * * | * * | 8673.3H* Nov 25, 16 * | * * | * * | 484.6H* 7.9M* |

" * " indicates that a Manual Next Due is set.

| COMM AM assy (#1) - Assembly - PN: |
| --- |
| Component/Action | Make/Model | Part No. | Serial No. | Tracking No. | Limit | Perf. | Time at Inst. | Due | TTSC | TTSN | Rem. |
| COMM AM assy (#1) / | / |  |  |  |  |  |  |  |  |  |  |
| -- COMM AM (#1) / O/C 2300 | GARMIN/ GNC250 | 011-00082-00 | 82901427 | 19403 |  | 8073.3H Nov 25, 14 |  |  | 115.4H 16.1M | 706.8H |  |
| -- GPS/COMM (#1) / O/C 3400 | / |  |  |  |  |  |  |  |  |  |  |

" * " indicates that a Manual Next Due is set.

| COMM FM assy (#1) - Assembly - PN: |
| --- |
| Component/Action | Make/Model | Part No. | Serial No. | Tracking No. | Limit | Perf. | Time at Inst. | Due | TTSC | TTSN | Rem. |
| COMM FM assy (#1) / | / |  |  |  |  |  |  |  |  |  |  |
| -- VHF FM (#1) / O/C 2300 | TECHNISONIC INDUSTRIES LIMITED/ TFM 138 | 921012-1 | F4698 | 13580 |  | 8073.3H Nov 25, 14 |  |  | 115.4H 16.1M |  |  |

" * " indicates that a Manual Next Due is set.

| COMM FM assy (#2) - Assembly - PN: |
| --- |
| Component/Action | Make/Model | Part No. | Serial No. | Tracking No. | Limit | Perf. | Time at Inst. | Due | TTSC | TTSN | Rem. |
| COMM FM assy (#2) / | / |  |  |  |  |  |  |  |  |  |  |
| -- VHF FM (#2) / O/C 2300 | / |  |  |  |  |  |  |  |  |  |  |
| -- VHF/UHF/LO FM (#2) / O/C 2300 | / |  |  |  |  |  |  |  |  |  |  |

" * " indicates that a Manual Next Due is set.

| CONVERTER 12V/USB charger (MinorMOD 2014-01) - Assembly - PN: |
| --- |
| Component/Action | Make/Model | Part No. | Serial No. | Tracking No. | Limit | Perf. | Time at Inst. | Due | TTSC | TTSN | Rem. |
| CONVERTER 12V/USB charger (MinorMOD 2014-01) / OC 2500 | / AS350/355 |  |  |  |  |  |  |  |  |  |  |
| -- - 600-HR, brackets/harnesses (MinorMOD 2014-01) / Ins 0500 | / |  |  |  | 600.0H | 8173.0H Oct 20, 15 |  | 8773.0H | 15.7H 5.3M |  | 584.3H |

" * " indicates that a Manual Next Due is set.

| ELT 406AF - Assembly - PN: S1840501-01 SN: 2620138-0021 |
| --- |
| Component/Action | Make/Model | Part No. | Serial No. | Tracking No. | Limit | Perf. | Time at Inst. | Due | TTSC | TTSN | Rem. |
| ELT 406AF / 12M 2500 | KANNAD/ 406 AF-COMPACT | S1840501-01 | 2620138-0021 | 24682 | 12.0M | 8156.6H Sep 24, 15 | 0.0H 0.0 | Sep 24, 16 | 32.1H 6.2M |  | 5.8M |
| -- ELT 406AF / Ops 0500 | / |  |  |  | 1.0M | 8188.7H Mar 14, 16 |  | Apr 14, 16 | 0.0H 0.5M |  | 0.5M |
| -- ELT 406AF, Battery / Ret 2500 | / |  |  |  | 72.0M | Sep 24, 15 |  | Sep 24, 21 | 6.2M |  | 65.8M |

" * " indicates that a Manual Next Due is set.

| ENGINE INLET AIR FILTER SYSTEM (STC SR01049SE) - Assembly - PN: |
| --- |
| Component/Action | Make/Model | Part No. | Serial No. | Tracking No. | Limit | Perf. | Time at Inst. | Due | TTSC | TTSN | Rem. |
| ENGINE INLET AIR FILTER SYSTEM (STC SR01049SE) / 7200 | FDC/Aerofilter/ AS350/355 |  |  |  |  |  |  |  |  |  |  |
| -- - 100-HR (STC SR01049SE) / Ins 0500 | / |  |  |  | 100.0H 12.0M | 8173.0H Oct 20, 15 |  | 8273.0H Oct 20, 16 | 15.7H 5.3M |  | 84.3H 6.7M |
| -- - 12M (STC SR01049SE) / Ins 0500 | / |  |  |  | 12.0M | 8173.0H Oct 20, 15 |  | Oct 20, 16 | 15.7H 5.3M |  | 6.7M |
| -- - 300-HR (STC SR01049SE) / Ins 0500 | / |  |  |  | 300.0H 12.0M | 8173.0H Oct 20, 15 |  | 8473.0H Oct 20, 16 | 15.7H 5.3M |  | 284.3H 6.7M |
| -- ENGINE AIR FILTER ELEM INTAKE (STC SR01049SE) / Ins 7100 | / | 1350A2-1 | 05347 | 8594 | 100.0H | 8173.0H Oct 20, 15 |  | 8273.0H | 15.7H 5.3M |  | 84.3H |

" * " indicates that a Manual Next Due is set.

| ENGINE instruments - Assembly - PN: |
| --- |
| Component/Action | Make/Model | Part No. | Serial No. | Tracking No. | Limit | Perf. | Time at Inst. | Due | TTSC | TTSN | Rem. |
| ENGINE instruments / O/C | / |  |  |  |  |  |  |  |  |  |  |
| -- NG TACH ind. / O/C 7700 | / | 704A47-612-042 |  |  |  |  |  |  |  |  |  |
| -- T4 ind. / O/C 7700 | / |  |  |  |  |  |  |  |  |  |  |
| -- TORQUEMETER ind. / O/C 7700 | / |  |  |  |  |  |  |  |  |  |  |

" * " indicates that a Manual Next Due is set.

| EPICYCLIC (3000-HR) - Assembly - PN: 350A32-0100-10 SN: M552 |
| --- |
| Component/Action | Make/Model | Part No. | Serial No. | Tracking No. | Limit | Perf. | Time at Inst. | Due | TTSC | TTSN | Rem. |
| EPICYCLIC (3000-HR) / Ove 6320 | / | 350A32-0100-10 |  |  | 3000.0H 288.0M | 8073.3H Apr 15, 14 |  | 11073.3H Apr 15, 38 | 115.4H 23.5M | 4086.0H | 1600H 222.5M |
| -- -Planet gear (#1) / Ret 6300 | / | 350A32-1082-03 |  |  | 20000.0H | 8073.3H Nov 25, 14 | 0.0H | 28073.3H | 115.4H 16.1M |  | 13500H |
| -- -Planet gear (#2) / Ret 6300 | / | 350A32-1082-03 |  |  | 20000.0H | 8073.3H Nov 25, 14 | 0.0H | 28073.3H | 115.4H 16.1M |  | 13500H |
| -- -Planet gear (#3) / Ret 6300 | / | 350A32-1082-03 |  |  | 20000.0H | 8073.3H Nov 25, 14 | 0.0H | 28073.3H | 115.4H 16.1M |  | 13500H |
| -- -Planet gear (#4) / Ret 6300 | / | 350A32-1082-03 |  |  | 20000.0H | 8073.3H Nov 25, 14 | 0.0H | 28073.3H | 115.4H 16.1M |  | 13500H |
| -- -Planet gear (#5) / Ret 6300 | / | 350A32-1082-03 |  |  | 20000.0H | 8073.3H Nov 25, 14 | 0.0H | 28073.3H | 115.4H 16.1M |  | 13500H |
| -- -Planet gear cage (54000) / Ret 6300 Cycle Name : TORQUE CYCLES | / | 350A32-1103-21 |  |  | 54000.0C | Nov 25, 14 22334.0C | 15339.0C | 60995.0C | 16.1M 15576.0C |  | 38424.0C |

" * " indicates that a Manual Next Due is set.

| FILTER, lubrication oil scavenge KIT (STC SH92-36) - Assembly - PN: 1741320 |
| --- |
| Component/Action | Make/Model | Part No. | Serial No. | Tracking No. | Limit | Perf. | Time at Inst. | Due | TTSC | TTSN | Rem. |
| FILTER, lubrication oil scavenge KIT (STC SH92-36) / 2500 | PUROLATOR FACET INC./ AS350B/BA/B2/B3 | 1741320 |  |  |  |  |  |  |  |  |  |
| -- - Bypass Indicator (STC SH92-36) / Tes 0500 | / |  |  |  | 750.0H 12.0M | 8173.0H Oct 20, 15 |  | 8923.0H Oct 20, 16 | 15.7H 5.3M |  | 734.3H 6.7M |

" * " indicates that a Manual Next Due is set.

| FIRE EXTINGUISHER (SLL=120M) - Assembly - PN: A1600 SN: |
| --- |
| Component/Action | Make/Model | Part No. | Serial No. | Tracking No. | Limit | Perf. | Time at Inst. | Due | TTSC | TTSN | Rem. |
| FIRE EXTINGUISHER (SLL=120M) / Ret 2600 | / | A1600 |  | 24998 | 120.0M | 8073.3H Dec 31, 14 |  | Dec 31, 24 | 115.4H 14.9M |  | 105.1M |
| -- - FIRE EXTINGUISHER (120M) - (12m) / Ins 2600 | / |  |  |  | 12.0M | 8156.6H Sep 24, 15 |  | Sep 24, 16 | 32.1H 6.2M |  | 5.8M |

" * " indicates that a Manual Next Due is set.

| FUEL CONTROL UNIT (#1) - Assembly - PN: 4-301-288-06 SN: 50210 |
| --- |
| Component/Action | Make/Model | Part No. | Serial No. | Tracking No. | Limit | Perf. | Time at Inst. | Due | TTSC | TTSN | Rem. |
| FUEL CONTROL UNIT (#1) / Ove 7300 **Linked AD: SB LTS101-73-20-0272 R2 | HONEYWELL/ 2549165-1H+X | 4-301-288-06 | 50210 | 23489 | 2400.0H | 8132.4H Jul 24, 15 | 1194.6H | 9337.8H | 1250.9H 8.2M |  | 1149.1H |
| -- - SB 0272 (#1) / Bea 0500 | / |  |  |  | 600.0H | 8132.4H | 1.7H | 8730.7H | 58.0H |  | 542.0H |

" * " indicates that a Manual Next Due is set.

| FUEL PUMP - (600-hr) (#1) - Assembly - PN: 4-301-377-01 SN: 0AFP826 |
| --- |
| Component/Action | Make/Model | Part No. | Serial No. | Tracking No. | Limit | Perf. | Time at Inst. | Due | TTSC | TTSN | Rem. |
| FUEL PUMP - (600-hr) (#1) / Ove 7300 | / | 4-301-377-01 | 0AFP826 |  | 2400.0H | 8073.3H | 104.4H | 10368.9H | 219.8H |  | 2180.2H |
| -- - SB 0203 (#1) / Ins 0500 | / | 4-301-377-01 | 0AFP826 |  | 600.0H | 8073.3H | 104.4H | 8568.9H | 219.8H |  | 380.2H |

" * " indicates that a Manual Next Due is set.

| G.P. MODULE (#1) - Assembly - PN: 4-101-000-44 SN: W81K035 |
| --- |
| Component/Action | Make/Model | Part No. | Serial No. | Tracking No. | Limit | Perf. | Time at Inst. | Due | TTSC | TTSN | Rem. |
| G.P. MODULE (#1) / Ins 7240 **Linked AD: SB LT101-72-30-0273 | / | 4-101-000-44 | W81K035 |  | 1800.0H | 8073.3H | 339.1H | 9534.2H | 454.5H |  | 1345.5H |
| -- - #1 Bearing, GP (#1) / O/C | / . | 4-301-242-03 | 0255 |  |  | 8073.3H | 5888.5H |  | 6003.9H | 6981.4H |  |
| -- - #1 seal, GP (#1) / O/C | / . | 4-304-047-01 | 12-162337-00181 |  |  | 8073.3H | 339.1H |  | 454.5H |  |  |
| -- - #2 Bearing, GP (#1) / O/C | / . | 4-301-518-01 | 970633103666 |  |  | 8073.3H | 4498.7H |  | 4614.1H | 4274.4H |  |
| -- - Axial comp. disc, GP (#1) / Ret Cycle Name : ENG_#1_NG | / . | 4-101-006-39 | 11-156107-000385 |  | 15000.0H 25000.0C | 8073.3H 9856.7C | 339.1H 488.8C | 22734.2H 34367.9C | 454.5H 607.9C |  | 14545.5H 24392.1C |
| -- - Compressor shaft, GP (#1) / Ret Cycle Name : ENG_#1_NG | / . | 4-101-007-12 | 84A006 |  | 15000.0H 25000.0C | 8073.3H 9856.7C | 3148.5H 4198.0C | 19924.8H 30658.7C | 3263.9H 4317.1C |  | 11736.1H 20682.9C |
| -- - Gas generator nozzle, GP (#1) / OC | / . | 4-111-090R24 | 010402300285 |  |  | 8073.3H 9856.7C | 854.0C |  | 115.4H -9002.7C |  |  |
| -- - GP disc (#1) / Ret Cycle Name : ENG_#1_NG | / . | 4-111-015-14 | BK7295 |  | 5000.0H 6300.0C | 8073.3H 9856.7C | 2647.5H 3427.0C | 10425.8H 12729.7C | 2762.9H 3546.1C |  | 2237.1H 2753.9C |
| -- - GP sealing plate (#1) / Ret Cycle Name : ENG_#1_NG | / . | 4-111-019-08 | 436797 |  | 15000.0H 25000.0C | 8073.3H 9856.7C | 2647.5H 3427.0C | 20425.8H 31429.7C | 2762.9H 3546.1C |  | 12237.1H 21453.9C |
| -- - Gp spacer (#1) / Ret Cycle Name : ENG_#1_NG | / . | 4-111-018-05 | SC52490 |  | 15000.0H 15000.0C | 8073.3H 9856.7C | 2647.5H 3427.0C | 20425.8H 21429.7C | 2762.9H 3546.1C |  | 12237.1H 11453.9C |
| -- - GP turbine blades (#1) / O/C | / . | 4-111-014-6X |  |  |  | 8073.3H | 684.5H |  | 799.9H |  |  |
| -- - Impeller, GP (#1) / Ret Cycle Name : ENG_#1_NG | / . | 4-101-052-64 | 012016500030 |  | 15000.0H 10000.0C | 8073.3H 9856.7C | 3485.7H 5477.1C | 19587.6H 14379.6C | 3601.1H 5596.2C |  | 11398.9H 4403.8C |

" * " indicates that a Manual Next Due is set.

| HYD. OIL FILTER (p/n 157152) - Assembly - PN: 157152 |
| --- |
| Component/Action | Make/Model | Part No. | Serial No. | Tracking No. | Limit | Perf. | Time at Inst. | Due | TTSC | TTSN | Rem. |
| HYD. OIL FILTER (p/n 157152) / Ret 2900 | / | 157152 |  |  | 1200.0H 48.0M | 7916.0H May 18, 13 | 0.0H | 9116.0H May 18, 17 | 272.7H 34.4M |  | 927.3H 13.6M |
| -- - HYD. OIL FILTER (p/n 157152) / Ins 2900 | / | 157152 |  |  | 600.0H 24.0M | 8092.0H May 5, 15 |  | 8692.0H May 5, 17 | 96.7H 10.8M |  | 503.3H 13.2M |

" * " indicates that a Manual Next Due is set.

| HYDRAULIC PUMP DRIVE assy - Assembly - PN: 350A35-0131-00 |
| --- |
| Component/Action | Make/Model | Part No. | Serial No. | Tracking No. | Limit | Perf. | Time at Inst. | Due | TTSC | TTSN | Rem. |
| HYDRAULIC PUMP DRIVE assy / OC 2900 | AIRBUS HELICOPTERS/ AS350D,BA,B2 | 350A35-0131-00 |  |  |  |  |  |  |  |  |  |
| -- - BEARING, greasable / Ret 2900 | / | 593733 | R/NA7571 |  | 3600.0H 72.0M | 7556.0H Feb 24, 12 | 0.0H | 11156.0H Feb 24, 18 | 632.7H 49.2M |  | 2967.3H 22.8M |

" * " indicates that a Manual Next Due is set.

| MAIN ROTOR MAST ASSY - Assembly - PN: 350A37-0003-05 SN: M1335 |
| --- |
| Component/Action | Make/Model | Part No. | Serial No. | Tracking No. | Limit | Perf. | Time at Inst. | Due | TTSC | TTSN | Rem. |
| MAIN ROTOR MAST ASSY / O/C 623000 | / | 350A37-0003-05 | M1335 | 17756 |  | Nov 25, 14 |  |  | 16.1M |  |  |
| -- -Main rotor shaft (A) / Ret 623000 Cycle Name : TORQUE CYCLES | / | 350A37-1076-10 | M3436 |  | 20000.0H 120000.0C | 8073.3H Nov 25, 14 22334.0C | 3970.6H 8.6 15339.0C | 24102.7H 126995.0C | 4086.0H 24.7M 15576.0C |  | 15914.0H 104424.0C |
| -- -Non-rotating swashplate / O/C 623000 | / | 350A37-1002-06 | PMA346 |  |  | 8073.3H Nov 25, 14 | 3970.6H 8.6 |  | 4086.0H 24.7M |  |  |
| -- -Rotating swashplate / O/C 623000 | / | 350A37-1003-07 | PMA411 |  |  | 8073.3H Nov 25, 14 | 3970.6H 8.6 |  | 4086.0H 24.7M |  |  |
| -- -Rotor shaft lower casing / O/C 623000 | / | 350A37-1195-02 | PMA148 |  |  | 8073.3H Nov 25, 14 | 3970.6H 8.6 |  | 4086.0H 24.7M |  |  |
| -- -Rotor shaft upper casing / O/C 623000 | / | 350A37-1196-09 | PMA82 |  |  | 8073.3H Nov 25, 14 | 3970.6H 8.6 |  | 4086.0H 24.7M |  |  |
| -- -SB05.00.32, shaft corrosion insp. / Ins | / |  |  |  | 72.0M | 8073.3H May 6, 14 |  | May 6, 20 | 115.4H 22.8M |  | 49.2M |
| -- -Scissor drive adapter / O/C 623000 | / | 350A37-1119-21 | PMA271 |  |  | 8073.3H Nov 25, 14 | 3970.6H 8.6 |  | 4086.0H 24.7M |  |  |
| -- -Scissor link, lower (#1) / O/C 623000 | / | 350A37-1126-01 | PMA1087 |  |  | 8073.3H Nov 25, 14 | 3970.6H 8.6 |  | 4086.0H 24.7M |  |  |
| -- -Scissor link, lower (#2) / O/C 623000 | / | 350A37-1126-01 | PMA1803 |  |  | 8073.3H Nov 25, 14 | 3970.6H 8.6 |  | 4086.0H 24.7M |  |  |
| -- -Scissors link, upper (#1) / O/C 623000 | / | 350A37-1127-01 | PMA1639 |  |  | 8073.3H Nov 25, 14 | 3970.6H 8.6 |  | 4086.0H 24.7M |  |  |
| -- -Scissors link, upper (#2) / O/C 623000 | / | 350A37-1127-01 | PMA1720 |  |  | 8073.3H Nov 25, 14 | 3970.6H 8.6 |  | 4086.0H 24.7M |  |  |
| -- -Swashplate bearing / Ret 623000 | / | Y51BB10843S2M74 | NR2972 |  | 4800.0H | 8073.3H Nov 25, 14 | 3970.6H 8.6 | 8902.7H | 4086.0H 24.7M |  | 714.0H |

" * " indicates that a Manual Next Due is set.

| MGB BEVEL REDUCTION GEAR - Assembly - PN: 350A32-0300-05N SN: M2240 |
| --- |
| Component/Action | Make/Model | Part No. | Serial No. | Tracking No. | Limit | Perf. | Time at Inst. | Due | TTSC | TTSN | Rem. |
| MGB BEVEL REDUCTION GEAR / Ove 6300 | / | 350A32-0300-05N | M2240 | 17768 | 3500.0H 288.0M | 8073.3H Dec 7, 10 | 991.3H | 10582.0H Dec 7, 34 | 1106.7H 63.7M | 7917.1H | 2393.3H 224.3M |
| -- -MGB bevel gear (#2) / Ret 6320 | / | 350A32-3173-20 | L4534 |  | 20000.0H | 8073.3H Nov 25, 14 | 991.3H 8.6 | 27082.0H | 1106.7H 24.7M |  | 18893.3H |
| -- -MGB bevel wheel (#2) / Ret 6320 | / | 350A32-3166-20 | L2286 |  | 20000.0H | 8073.3H Nov 25, 14 | 991.3H 8.6 | 27082.0H | 1106.7H 24.7M |  | 18893.3H |
| -- -MGB bottom casing (#1) / O/C 6320 | / | 350A32-3119-05 | MAP38 |  |  | 8073.3H Nov 25, 14 | 7801.7H 8.6 |  | 7917.1H 24.7M |  |  |
| -- MGB Main casing / O/C 6300 | / | 350A32-3121-04 | MAP5021 |  |  | 8073.3H Nov 25, 14 | 7801.7H 212.9 |  | 7917.1H 229.0M | 7917.1H |  |
| -- OIL FILTER, MGB / Ret | CHAMPION AEROSPACE/ | CH48108-1 | 1213492468 | 24792 | 600.0H 24.0M | 8073.3H Nov 25, 14 |  | 8673.3H Nov 25, 16 | 115.4H 16.1M |  | 484.6H 7.9M |
| -- OIL, MGB (MOBIL 254) / Rep | / | MOBIL-254 |  |  | 600.0H 24.0M | 8073.3H Nov 25, 14 |  | 8673.3H Nov 25, 16 | 115.4H 16.1M |  | 484.6H 7.9M |

" * " indicates that a Manual Next Due is set.

| P.T GOVERNOR (#1) - Assembly - PN: 4-301-289-05 SN: 31107 |
| --- |
| Component/Action | Make/Model | Part No. | Serial No. | Tracking No. | Limit | Perf. | Time at Inst. | Due | TTSC | TTSN | Rem. |
| P.T GOVERNOR (#1) / Ove 7300 **Linked AD: 2011-23-13, SB LTS101-73-20-A0268 R2 | / | 4-301-289-05 | 31107 |  | 2400.0H | 8073.3H Dec 9, 14 | 37.9H | 10435.4H | 153.3H 15.7M |  | 2246.7H |
| -- - AD2011-23-13 (#1) / Bea 0500 | / |  |  |  | 900.0H | 8073.3H Nov 25, 14 | 37.9H | 8935.4H | 153.3H 16.1M |  | 746.7H |

" * " indicates that a Manual Next Due is set.

| P.T. MODULE (#1) - Assembly - PN: 4-141-000-78 SN: W81K035 |
| --- |
| Component/Action | Make/Model | Part No. | Serial No. | Tracking No. | Limit | Perf. | Time at Inst. | Due | TTSC | TTSN | Rem. |
| P.T. MODULE (#1) / Ins 7250 **Linked AD: SB LTS 101-79-20-0248 R2 | / | 4-141-000-78 | W81K035 |  | 1800.0H | 8073.3H | 339.1H | 9534.2H | 454.5H | 7875.4H | 1345.5H |
| -- - #2 Seal, PT (#1) / O/C | / . | 4-301-357-04 | 11-152826-61283 |  |  | 8073.3H | 684.5H |  | 799.9H | 460.8H |  |
| -- - #3 Seal, PT (#1) / O/C | / . | 4-310-448-01 | NSN |  |  | 8073.3H | 3485.7H |  | 3601.1H |  |  |
| -- -#2 bearing outer race (#1) / O/C | / . | 4-141-440-01 | K765 |  |  | 8073.3H | 5538.5H |  | 5653.9H | 5314.8H |  |
| -- -#3 bearing (#1) / O/C | / . | 4-301-242-03 | 031991414872 |  |  | 8073.3H | 2617.1H |  | 2732.5H | 2393.4H |  |
| -- -Combustor liner (#1) / O/C | / . | 4-131-010-30 | 05P14391 |  |  | 8073.3H | 684.5H |  | 799.9H | 460.8H |  |
| -- -PT nozzle (#1) / O/C | / . | 4-141-060-16 | A357 |  |  | 8073.3H |  |  | 115.4H | 3262.0H |  |
| -- -PT rotor assy (#1) / Ret Cycle Name : ENG_#1_NP | / . | 4-141-290-18 | SC46952 |  | 12000.0H 11000.0C | 8073.3H 16553.9C | 2068.2H 3986.4C | 18005.1H 23567.6C | 2183.6H 4203.6C |  | 9816.4H 6796.4C |
| -- -RBSH (#1) / O/C | / . | 4-143-020-43 | 11-101978-00413 |  |  | 8073.3H | 339.1H |  | 454.5H |  |  |

" * " indicates that a Manual Next Due is set.

| T/R D/S REAR SECTION - Assembly - PN: 350A34-0110-05 SN: U/K |
| --- |
| Component/Action | Make/Model | Part No. | Serial No. | Tracking No. | Limit | Perf. | Time at Inst. | Due | TTSC | TTSN | Rem. |
| T/R D/S REAR SECTION / O/C 6500 | / | 350A34-0110-05 | U/K | 33949 |  | 8173.0H Oct 20, 15 |  |  | 15.7H 5.3M |  |  |
| -- - AFT shaft / Ret 6500 | / | 350A34-1011-XX | U/K |  | 20000.0H | 8173.0H Oct 20, 15 | 6739.7H 0.4 | 21433.3H | 6755.4H 5.7M | 6755.4H | 13244.6H |
| -- BEARING, TR D/S, 6x / Ret 6500 | / | 593404 |  |  | 3600.0H 60.0M | 8173.0H Oct 20, 15 | 580.2H 30.1 | 11192.8H Apr 17, 18 | 595.9H 35.4M | 595.9H | 3004.1H 24.6M |

" * " indicates that a Manual Next Due is set.

| T/R SPIDER assy - Assembly - PN: 350A33-2030-00 SN: M1545 |
| --- |
| Component/Action | Make/Model | Part No. | Serial No. | Tracking No. | Limit | Perf. | Time at Inst. | Due | TTSC | TTSN | Rem. |
| T/R SPIDER assy / O/C 6500 | / | 350A33-2030-00 | M1545 |  |  | 5498.9H |  |  | 2689.8H | 10093.3H |  |
| -- T/R PITCH CHANGE BEARING / Ret 6500 | / | 704A33-651-210 | 3383 |  | 3000.0H | 5498.9H | 0.0H | 8498.9H | 2689.8H |  | 310.2H |

" * " indicates that a Manual Next Due is set.

| TGB ASSY - Assembly - PN: 350A33-0200-05 SN: MA0311 |
| --- |
| Component/Action | Make/Model | Part No. | Serial No. | Tracking No. | Limit | Perf. | Time at Inst. | Due | TTSC | TTSN | Rem. |
| TGB ASSY / Ove 652000 | / | 350A33-0200-05 | MA0311 |  | 3000.0H 288.0M | 7259.9H May 25, 11 | 0.0H | 10259.9H May 25, 35 | 928.8H 58.1M | 7062.4H | 2071.2H 229.9M |
| -- - Bevel gear TGB / Ret 652001 | / | 350A33-1000-21 | ZF5315 |  | 20000.0H | 7259.9H | 6133.6H | 21126.3H | 7062.4H |  | 12937.6H |
| -- - Bevel wheel TGB / Ret 652002 | / | 350A33-1001-21 | ZF4175 |  | 20000.0H | 7259.9H | 6133.6H | 21126.3H | 7062.4H |  | 12937.6H |
| -- - Casing TGB / Ret 652003 | / | 350A33-1090-01 | MA0119 |  | 20000.0H | 7259.9H | 6133.6H | 21126.3H | 7062.4H |  | 12937.6H |
| -- - Control lever TGB (B) / Ins 6500 | / | 350A33-1058-03 | MA04887 |  | 660.0H | 7840.6H | 0.0H | 8500.6H | 348.1H |  | 311.9H |
| -- - Tail rotor shaft TGB / Ret 652004 | / | 350A33-1092-01 | MA30422 |  | 20000.0H | 7259.9H | 0.0H | 27259.9H | 928.8H |  | 19071.2H |
| -- OIL, TGB (Mobil 254) / Rep | / | MOBIL 254 |  |  | 600.0H | 8073.3H Nov 25, 14 |  | 8673.3H | 115.4H 16.1M |  | 484.6H |

" * " indicates that a Manual Next Due is set.

| This report has been prepared by: |
| --- |
| Signature | License Number | Date |
| © Aircraft Maintenance Systems RD inc |